## Slide 1: CPEN 211: Introduction to Microcomputers Slide Set 13: Caches and Virtual Memory
Prof. Tor Aamodt
[Background: Portion of Intel Core i7-5960X Extreme Edition 20 MB L3 Cache;
Source: https://www.anandtech.com/show/8426/the-intel-haswell-e-cpu-review-core-i7-5960x-i7-5930k-i7-5820k-tested]
Notes: 1

## Slide 2: Learning Objectives
After this lecture you should be able to:
  Explain the motivation for using caches and describe levels of the memory hierarchy
  Define simple cache terminology and explain operation of several types of cache
  Calculate relationship between cache parameters; evaluate which accesses will hit or miss out of a sequence of accesses; evaluate performance impact of caches using a simple analytical model
  Explain the motivation for using virtual memory.
  Explain what a page table is and how it is used to implement virtual memory. Explain what a translation look aside buffer (TLBs) is and how it operates. Explain interaction of TLBs and caches (virtual indexed physically tagged cache, synonym problem)

## Slide 3: Reading
COD ARM Edition Chapter 5

## Slide 4: How to Design “Memory” Blocks?

## Slide 5: Magnetic storage?
E.g., HP Ultrium. Sequential access 1TB/hour. 3TB cartridge cost (circa 2016) $32.95 @ Office Depot (93 GB per $)
Tape: lowest cost per bit… low bandwidth,
Problem w/ Tape: instructions & data not accessed sequentially
[image source: http://news.bbc.co.uk/2/hi/technology/7908666.stm ]

## Slide 6: Random Access Memory
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
3
011
010
64x1-bit RAM: value at address “011010” = 1
1
decoder
mux

## Slide 7: Static RAM
Single ported SRAM uses six to store a single bit.
How many transistors in a master-slave D flip-flop (Flipped Lecture 2)?
A: 6
B: 16
C: 34 ✔︎
D: 48
E: Not sure
How many transistors in a master-slave D flip-flop (Flipped Lecture 2)?
A: 6
B: 16
C: 34
D: 48
E: Not sure

## Slide 8: SRAM Tradeoffs
Small SRAM is very fast
~200 picosecond access time for 4096 byte SRAM at 32 nm (single cycle access 5GHz)
Large SRAM much slower
~5 nanosecond access time for 32 MB SRAM at 32 nm (25 cycle access at 5 GHz)

## Slide 9: Dynamic RAM
DRAM uses single transistor and capacitor to store a bit.
DRAM Module
DRAM chips
[Courtesy: Onur Mutlu, ETH Zurich]

## Slide 10: DRAM Chip Internals [Onur Mutlu, ETH Zurich]
Control Logic
I/O
Peripheral Circuitry
Bitline
S
S
S
S
Sense amplifiers
(row buffer)
Wordline
DRAM Cell
Bank
DRAM Array
Off-chip channel

## Slide 11: DRAM Operations [Onur Mutlu, ETH Zurich]
ACTIVATE: Store the row into the row buffer
READ: Select the target cache line and drive to CPU
PRECHARGE: Prepare the array for a new ACTIVATE
1
1
1
1
1
2
3
to I/O
What is the minimum number of DRAM commands to read from three different rows?
A: 3
B: 6
C: 8 ︎ ✔︎
D: 9
E: Not sure
What is the minimum number of DRAM commands to read from three different rows?
A: 3
B: 6
C: 8
D: 9
E: Not sure

## Slide 12: DRAM Access Latency [Onur Mutlu, ETH Zurich]
Command
Data
Duration
ACTIVATE
READ
PRECHARGE
1
1
1
1
Cache line (64B)
Next
ACT
Activation latency (13ns / 50 cycles)
1
Precharge latency (13ns / 50 cycles)
2

## Slide 13: DRAM Tradeoffs
Cheaper than SRAM but more expensive than disk or tape: E.g., “16GB Corsair DDR3-2000” for $243.13 on shop.ca ($15 per GB --1395 times more per bit versus tape).
Longer access time than SRAM
DDR3-2000 minimum latency is 9 ns

## Slide 14: Flash Memory
NOR:
NAND:
[image source: https://en.wikipedia.org/wiki/Flash_memory ]

## Slide 15: Fundamental Problem
Faster memory is smaller.
At this point, we know how to design a very fast computer that uses a very small memory.
How can we design a fast computer that can use large memory?

## Slide 16: The Memory Wall
CPU-DRAM Gap
1980: no cache in µproc; 1995 2-level cache on chip (1989 first Intel µproc with a cache on chip)
µProc
60%/yr.
DRAM
7%/yr.
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
“Moore’s Law”
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 17: Solution: Memory Hierarchy
Regs
L1-Cache
L2-Cache
Memory
Disk, Tape, etc.
Bigger
Faster

## Slide 18: What do real programs do?
Consider “SAXPY” loop:
void saxpy( float a, float *X, float *Y, unsigned N )
{
for( i=0; i < N; i++ )
Y[i] = a*X[i] + Y[i];
}
Two observations:
1. Read then write Y[i] (temporal locality)
2. Read X[0], then X[1], then X[2] (spatial locality)

## Slide 19: A Silly Locality Analogy
Slow RAM: Is book in UBC library?
Fast RAM: Is book I want in backpack?
Disk: inter-library loan (or chapters.ca)
Temporal Locality (analogy):
If use book once, likely to
use it again soon.
Spatial Locality (analogy):
If last time went to library
borrowed book on “mystery
novels” next time likely get
another book from same
section.

## Slide 20: Temporal Locality
Temporal Locality: After accessing single location once the program accesses it again.
Example: Y[i] = a*X[i] + Y[i];
1: FLDS S3,[R1] ; read X[i]
2: FMULS S5,S3,S4 ; a*X[i]
3: FLDS S6,[R2] ; read Y[i]
4: FADDS S7,S5,S6 ; a*X[i]+Y[i]
5: FSTS S7,[R2] ; write Y[i]
line 3: read Y[i]
line 5: write Y[i] (note: same location)

## Slide 21: Exploiting Temporal Locality
Idea: When accessing location (address) make copy of data in small fast memory. If there is temporal locality program will (likely) try to access the same data again soon.
Large slow memory
Small fast memory
Y[0]

## Slide 22: How is data transferred?
Option 1: Software moves data
  Small fast RAM called a “scratchpad” memory
  Used by recent GPUs
  Typically, the programmer must decide when to move data between slow big memory and fast small memory. Add extra code to move data.
  Benefits: Programmer can optimize what to put in fast memory and when.
  Drawbacks: More work for programmer
Option 2: Hardware managed cache
  Most CPUs take this approach. Our focus.

## Slide 23: Hardware managed cache design
We will have hardware automatically copy data to “cache” when program accesses the location holding that data.
Problem: Need mechanism for hardware to find data next time program accesses it.
Solution: Save address (“tag”) in cache along with copy of the data at that address.

## Slide 24: First level caches in typical pipeline
Instruction
Cache
Data
Cache
First level caches
(separate to avoid
structural hazard)

## Slide 25: Example
Show cache contents when executing following code on “fully associative” data cache with two 4 byte blocks.
FLDS S3,[R2] ; read Y[i]
FADDS S4,S2,S3 ; a*X[i]+Y[i]
FSTS S4,[R2] ; write Y[i]
Initially: Regs[R2]=0x8, Regs[S2]=78.2, memory state:
Address | Memory contents | Description
0x0000000c | C4 7A 00 00 | Y[3] = -1000.0
0x00000008 | 40 2D F8 54 | Y[2] = 2.718282
0x00000004 | 40 49 0F DB | Y[1] = 3.141593
0x00000000 | 42 28 00 00 | Y[0] = 42.0

## Slide 26: Example, continued…
Each row in cache contains four fields:
  “data” holds copy of memory data
  “tag” indicates address associated with data
  “modified” indicates if data in cache was written to since copying from memory
  “valid” indicates the row contains valid information.
valid? | modified? |  | tag | data
0 | 0 |  | 0x00000000 | 00 00 00 00
0 | 0 |  | 0x00000000 | 00 00 00 00
cache holding two 4-byte “blocks”

## Slide 27: Example, continued
Executing:
FLDS S3,[R2] ; read Y[i]
Step 1: compute effective address of memory access R2 = 0x00000008
Step 2: Check if block containing contents of memory
at address 0x00000008 is present in cache:
Answer = no (“cache miss”). (If yes, “cache hit”)
valid? | modified? |  | tag | data
0 | 0 |  | 0x00000000 | 00 00 00 00
0 | 0 |  | 0x00000000 | 00 00 00 00

## Slide 28: Example, continued
Address | Memory contents | Description
0x0000000c | C4 7A 00 00 | Y[3] = -1000.0
0x00000008 | 40 2D F8 54 | Y[2] = 2.718282
0x00000004 | 40 49 0F DB | Y[1] = 3.141593
0x00000000 | 42 28 00 00 | Y[0] = 42.0
valid? | modified? | tag | data
0 | 0 | 0x00000000 | 00 00 00 00
0 | 0 | 0x00000000 | 00 00 00 00
Executing:
FSTS S3,[R2] ; read Y[i]
Step 3: Copy data into cache (use block with “valid=0”)
valid? | modified? | tag | data
1 | 0 | 0x00000008 | 40 2D F8 F4
0 | 0 | 0x00000000 | 00 00 00 00
How many copies are there of the data “40 2D F8 F4” after Step 3?
A: 0
B: 1
C: 2 ︎ ✔︎
D: 3
E: Not sure
How many copies are there of the data “40 2D F8 F4” after Step 3?
A: 0
B: 1
C: 2
D: 3
E: Not sure

## Slide 29: Example, continued
Cache after executing
FADDS S4,S2,S3; Regs[F4]=80.918 (0x42A1D629)
FSTS S4,[R2]; write Y[i]
Address | Memory contents | Description
0x0000000c | C4 7A 00 00 | Y[3] = -1000.0
0x00000008 | 40 2D F8 54 | Y[2] = 2.718282
0x00000004 | 40 49 0F DB | Y[1] = 3.141593
0x00000000 | 42 28 00 00 | Y[0] = 42.0
valid? | modified? | tag | data
1 | 0 | 0x00000008 | 40 2D F8 F4
0 | 0 | 0x00000000 | 00 00 00 00
valid? | modified? | tag | data
1 | 1 | 0x00000008 | 42 A1 D6 29
0 | 0 | 0x00000000 | 00 00 00 00

## Slide 30: Question
Consider the following series of memory references (byte addresses, in decimal): 2, 3, 2, 8, 10, and 2.
Assume fully associative cache with 8 one-byte blocks that are initially empty (valid=0), label each reference in the list as a hit or a miss, report the total number of hits and show the final contents of the cache.
Ignore “modified” and “data” fields.

## Slide 31: Solution
Valid | Tag
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
Valid | Tag
1 | 2
1 | 3
1 | 8
1 | 10
0 | -
0 | -
0 | -
0 | -
2 m, 3 m, 2 h, 8 m, 10 m, 2 h
Valid | Tag
1 | 2
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
Valid | Tag
1 | 2
1 | 3
0 | -
0 | -
0 | -
0 | -
0 | -
0 | -
Valid | Tag
1 | 2
1 | 3
1 | 8
0 | -
0 | -
0 | -
0 | -
0 | -

## Slide 32: Problem with this design
  Where do we put data if cache is full?
Return to this question after considering spatial locality.

## Slide 33: Spatial Locality
Definition: After accessing a location program accesses nearby location.
Example:
Y[2] = a*X[2] + Y[2];
Y[3] = a*X[3] + Y[3];
Program reads Y[2], then Y[3].

## Slide 34: Exploiting Spatial Locality
When program accesses Y[2] transfer both Y[2] and Y[3].
In general, transfer a “block” of data (or instructions) at a time. Block size
typically 32 to 128 bytes.
In figure at left have a block containing Y[2] and Y[3] but more typical 64 byte block can hold sixteen 4-byte values.
Y[2], Y[3]
If we accessed Y[3] first what should hardware copy to cache?
A: Just Y[3]
B: Y[3] and Y[4]
C: Y[2] and Y[3] ✔︎
D: Not sure
If we accessed Y[3] first what should hardware copy to cache?
A: Just Y[3]
B: Y[3] and Y[4]
C: Y[2] and Y[3]
D: Not sure

## Slide 35: Cache Blocks (Cache Lines)
Want to move nearby data at same time to exploit spatial locality. Divide up memory into blocks that are power of two multiples of word size. Block starts at address aligned to block size (whole number multiple of block size).
0xfffffff8 | 00 00 00 00 00 00 00 00
0xfffffff0 | 00 00 00 00 00 00 00 00
… | …
0x00000010 | 01 00 70 95 42 3C E7 98
0x00000008 | C4 7A 00 00 40 2D F8 54
0x00000000 | 40 49 0F DB 42 28 00 00
memory
address
memory
contents
8 byte block. First byte at 0x00000008 contains “54”. Last byte at 0x0000000f contains “C4” (“little endian” byte order).
Copy entire block at once.
Which byte value is at address 0x00000009?
A: 98
B: 00
C: F8 ✔︎
D: C4
E: Not sure
Which byte value is at address 0x00000009?
A: 98
B: 00
C: F8
D: C4
E: Not sure

## Slide 36: Modified Cache Design
Increase data field size to hold block of size 8 bytes. Now cache can exploit both spatial and temporal locality.
valid? | modified? | tag | data
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00

## Slide 37: Block Size Impact on Tag
Blocks start at address aligned to block size.
This means lower log2(block size) bits of block address are always zero.
Would be a waste of transistors if we explicitly store these zero values.

## Slide 38: Question
For a fully associative cache with 16 byte blocks what is the tag in hex for a block with starting address 0x00008020?
What is the tag value?
A: 0x00008020
B: 0x0000
C: 0x000080
D: 0x0000802 ✔︎
E: Not sure
What is the tag value?
A: 0x00008020
B: 0x0000
C: 0x000080
D: 0x0000802
E: Not sure

## Slide 39: Example, revisited (FLDS F3, [R2])
0x00000010 | 01 00 70 95 42 3C E7 98
0x00000008 | C4 7A 00 00 40 2D F8 54
0x00000000 | 40 49 0F DB 42 28 00 00
memory
address
memory
contents
Regs[R2] = 0x00000008 implies tag=0x0000001 -- why?
In binary 0x00000008 = 0000 … 000000001000
Drop least significant 3 bits since using 8 byte blocks
Cache after executing
FLDS F3 [R2] ; read Y[i]
4 byte value written to Regs[F3] by FLDS is 0x402DF854
valid? | modified? | tag | data
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00
valid? | modified? | tag | data
1 | 0 | 0x00000001 | C4 7A 00 00 40 2D F8 54
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00
copy 8 byte block to cache
Would we copy C4 7A 00 00 into cache if block size was 4 bytes and read address 0x00000008?
A: Yes
B: No ✔︎
C: Not sure
Would we copy C4 7A 00 00 into cache if block size was 4 bytes and read address 0x00000008?
A: Yes
B: No
C: Not sure

## Slide 40: Multiple words in block
For the SAXPY loop 8 byte block contains two elements – e.g., Y[2] and Y[3]:
How to find specific data (e.g., Y[2] or Y[3]) accessed by load/store instruction?
valid? | modified? | tag | data
1 | 0 | 0x00000001 | C4 7A 00 00 40 2D F8 54
Y[3]
Y[2]

## Slide 41: Solution: Block Offset
Recall, block starts at address aligned to log2(block size) and data stored within block in same order as in memory.
So, we can compute location of word in block by using lower log2(block size) bits of address of word.

## Slide 42: Solution: Block Offset
Example block offset calculation (8 byte block)
address (hex) address (binary)
0x00000008 = 0000 … 000000001000
0x0000000C = 0000 … 000000001100
valid? | modified? | tag | data
1 | 0 | 0x00000001 | C4 7A 00 00 40 2D F8 54
Block Offset = 0
Block Offset = 4

## Slide 43: Question
For a cache with 16 byte blocks what is the block offset in hex for a 4 byte float stored in memory at starting address 0x00008028?
What is the block offset?
A: 0x00008028
B: 10002 ✔︎
C: 0x28
D: 002
E: Not sure
What is the block offset?
A: 0x00008028
B: 10002
C: 0x28
D: 002
E: Not sure

## Slide 44: Example, revisited
valid? | modified? | tag | data
1 | 1 | 0x00000001 | 42 A1 D6 29 C4 7A 00 00
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00
Regs[R2] = 0x8 => Tag=0x1, Block Offset=0
Cache after executing
FADDS S4,S2,S3 ; Regs[S4] = 0x42A1D629
FSTS S4,[R2] ; write Y[i]
valid? | modified? | tag | data
1 | 0 | 0x00000001 | C4 7A 00 00 40 2D F8 54
0 | 0 | 0x00000000 | 00 00 00 00 00 00 00 00

## Slide 45: What if cache is full?
So far we assumed we “fill” blocks into cache starting at first available (“invalid”) row and when accessing cache do parallel search for tag match in all rows (“fully associative”)
If cache full (no blocks are “invalid”), need to make space for new block by “evicting” a “valid” block from cache.

## Slide 46: Which block gets evicted?
Which is best block to evict? Recall we want to keep useful data in cache. So, we need to consider locality.
Provably optimal: evict block that will be accessed again furthest in future.
Problem: Hardware does not know future. Need prediction mechanism.

## Slide 47: How to predict?
Goal: Want to predict which block will be accessed furthest in future.
Observation: For many programs, the longer a block has not been accessed, the less likely it is that we will access it soon.
Can quantify this using “reuse distance”.

## Slide 48: Reuse Distance (Definition)
Consider sequence of memory accesses to blocks A, B, C, D, and E:
ABBCBCCDBBEDBBBA
Between two accesses to block A made 14 accesses to four unique blocks (B, C, D, E)
Reuse distance for A is four.

## Slide 49: Reuse distance measurement
Typically access recently used data most frequently.

## Slide 50: Replacement Policy
The algorithm used to decide which block to evict is called a “replacement policy”.
Observation on last slide suggests good replacement policy is to evict the “least recently used” (LRU) block.

## Slide 51: Least Recently Used
LRU Implementation?
  Naïve: add timestamp field to row updated each time block accessed. To evict, compare all timestamps to find smallest.
  In practice try to limit search to small number of blocks (e.g., “set associative” later in slides). With two blocks can use bit to indicate which one most recently used.
  Patents on approximate LRU (pseudo-LRU).
Random & FIFO get similar hit rates to LRU.
Recently, replacement policy very active area of innovation due to multicore and “big data”.

## Slide 52: Research
Subhasis Das, Tor M. Aamodt, William J. Dally Reuse Distance Based Probabilistic Cache Replacement,
in ACM Transactions on Architecture and Code Optimization (TACO),
Volume 12 Issue 4, Article No. 33 (Oct 2015), 22 pages.

## Slide 53: Question
Assume fully associative cache with 8 one-byte blocks. Consider the following series of memory references (byte addresses, in decimal): 2, 3, 2, 8, 10, and 2. After this sequence has been observed, what is the tag of the least recently used block?
What is the block offset?
A: 2
B: 3 ✔︎
C: 8
D: 10
E: Not sure
What is the block offset?
A: 2
B: 3
C: 8
D: 10
E: Not sure

## Slide 54: Fully Associative Implementation
=
4-bit tag comparison hardware

## Slide 55: Problem with Fully Associative
Comparing all tags in parallel is expensive (time, area and energy).
Can avoid multiple tag comparisons if block can only be stored in single row in cache. This is called “direct mapped”. Then, only one tag needs to be checked.
Also makes replacement decision easy (only one choice of what to evict).

## Slide 56: Direct Mapped Cache
Given start address of block need way for hardware to select single row of cache to place block in.
Start of block is aligned so least significant log2(block size) bits in address are zero. Use hash on remaining address bits to compute an index used to select row.
Typically, use next log2(number of rows) least significant bits of block start address as hash function: index = block address % num. rows

## Slide 57: Direct Mapped Cache
“Block Address” is starting address of block with log2(block size) least significant bits truncated (removed).
Address:
Index = (Block Address) modulo (Number of Rows)
Address:
Block Address Block Offset
Tag Index Block Offset

## Slide 58: Direct Mapped Cache
4-byte blocks, so block offset is 2-bits.
1024 rows so use log2(1024)=10-bits of address to select row. These bits are called “index”.
LDR R1, [R2, #8]

## Slide 59: Problem: Conflict Misses
Some “rows” (blocks) in direct mapped cache used more than others.
Data that index to these blocks may get evicted before reused even though there was enough space in cache to keep them.
Would like to have flexibility of fully associative without cost of parallel comparison of all tags in cache.

## Slide 60: Set Associative Cache
Index selects row containing set of blocks.
Search tags of all blocks in this set in parallel.

## Slide 61: Set Associative Cache

## Slide 62: Question
Consider the following series of memory references (byte addresses, in decimal): 2, 3, 2, 8, 10, and 2. Assuming first a direct mapped cache with one byte blocks and total capacity of 8 bytes, then a two-way set associative cache with 2-byte blocks and total size of 16 bytes that are initially empty. Label each reference in the list as a hit or a miss and show the final contents of the cache.

## Slide 63: Solution
Direct-mapped cache 2-way set associative
1 byte blocks 2 byte blocks
8 bytes total 16 bytes total
Cache set | Address
000 | 
001 | 
010 | 
011 | 
100 | 
101 | 
110 | 
111 | 
2 m, 3 m, 2 h, 8 m, 10 m, 2 m
Cache Set | Address
00 | { - , - }
01 | { - , - }
10 | { - , - }
11 | { - , - }
2 m, 3 h, 2 h, 8 m, 10 m, 2 h
2
3
2
8
10
2
[2,3]
[2,3]
[8,9]
[2,3]
[10,11]

## Slide 64: What happens on a write? Cache Writing Policies
Write-through
  Store to both cache and memory on every write
    Slow writes
  Conservative: memory always holds valid data
  Simple cache
Write-back
  Store to cache only
    Fast writes
  On write, mark data block in cache as dirty
    Need extra memory bit for each cache line (dirty bit)
  Memory may hold invalid/stale data (must fix!)
  More complex cache
Text: COD ARM Edition §5.3

## Slide 65: Write Misses (how are they handled by hardware?)
Writes can miss in cache… leads to a hardware design choice (the design choice options are answers to question “how do we deal with write miss”). Two choices are:
  Write-allocate
    First, read cache block from memory into cache
    Second, proceed with write
  No write-allocate
    Write to memory directly
    Memory access is slow, CPU must wait
    Improve performance using “write buffers” (see later)
Most common design choices:
  Writeback cache uses write-allocate
  Write-through cache uses no write-allocate (keep it simple)
Text: COD ARM Edition §5.3

## Slide 66: Counter-Intuitive Case 1: Load instruction may cause Writes
Write-back cache problems
  Over time, many cache blocks marked “dirty”
  Eventually, must write dirty data back to memory
    Usually, when cache block is evicted
    (Also, if cache is “flushed” for OS context switch)
  Called a “writeback” event
Load may cause writes
  Load instruction miss, may evict a dirty cache block
    Write first: (old) dirty cache block writes to memory
    Read second: (new) memory block loaded into cache
  …but CPU is waiting for read result to do Load…
    Many CPUs do the “read first”
    Holds dirty cache block in special “write buffer” during read
Text: COD ARM Edition §5.3

## Slide 67: Counter-Intuitive Case 2: Store instruction may cause Reads
Writes can miss in the cache!
Store may cause Reads
  Writeback cache with write-allocate policy
    Store misses in cache
    CPU performs READ from memory, puts data in cache
    CPU performs write in cache, marks block dirty
It can be even more complex
  When store misses in cache above
    Must evict existing cache block
    If marked dirty, must first write back the cache block to memory
  CPU performs read from memory
  CPU performs write in cache
Text: COD ARM Edition §5.3

## Slide 68: Write Buffers for Write-Through Caches
Q. Why a write buffer ?
Processor
Cache
Write Buffer
Lower Level Memory
Holds data awaiting write-through to
lower level memory
A. So CPU doesn’t stall
Q. Why a buffer, why not just one register ?
A. Bursts of writes are
common.
Q. Are Read After Write (RAW) hazards an issue for write buffer?
A. Yes! Drain buffer before next read, or send read after 1st checking write buffers.
Text: COD ARM Edition §5.3

## Slide 69: Performance / Multilevel Caches
Impact of caches on performance?
Reduce “Miss Penalty” by adding second-level of caching:
CPU
L1 $
L2 $
Memory
CPU
L1 $
Memory
1 cycle
200 cycles
1 cycle
10 cycles
200 cycles

## Slide 70: Example Problem
How much faster is a processor with both L1 and L2 caches versus a processor with only an L1 cache?
Assume the following:
  CPI is 1.0 when all memory references hit in the L1 cache.
  All instruction references hit in L1 instruction cache.
  Loads and stores comprise 30% of instructions.
  L1 data cache hit rate is 80%
  L2 data cache hit rate is 40% and a L2 cache hit takes 10 cycles.
  Main memory takes 200 cycles to access.

## Slide 71: Solution
(Adding L2 cache does not impact instruction count or cycle time)

## Slide 72: Solution, Continued…

## Slide 73: Solution, Continued…
0
1.48

## Slide 74: Virtual Memory
Next we look at the virtual memory system present on all modern computer systems.
We will see how virtual memory can lead to page faults in the normal operation of a program.
The motivation for virtual memory is that it simplifies software development by freeing the programmer from having to think about low level details when trying to get their program to run correctly

## Slide 75: Multiple Programs Using Memory
Computer has 1024 MB DRAM
  Internet Explorer (IE) uses 30 MB
  MS Word uses 20 MB
  Vista uses 1280 MB
  Total: 1330 MB
How to run all three programs at once?
It gets worse….
  Firefox assumes memory starts at address 0
  Word assumes memory starts at address 0
    How can they both run if they both assume memory starts at 0 ??
  Vista ? It’s the OS…. who knows!

## Slide 76: Multiple Programs Using Memory
It gets even worse
  Vista starts using 1280 MB
  IE starts using 30 MB
  Word starts using 20 MB
  User opens web page (cnn.com), IE wants + 72MB
  User opens document (ps3 soln) Word wants +30MB
  User opens 2nd web page(youtube), IE wants +40MB
  User edits document, Word wants +10MB
  TOTAL
    Vista 1280MB, IE 142 MB, Word 60 MB
Main
Mem
Vista
IE
Word
IE
IE
Word
Word

## Slide 77: How can we divide up memory between programs?
It gets even worse
  Exit Word
  Start engineering program
    Wants 300MB for a matrix
    Must be contiguous!
    How?
    Move IE? Not realistic
Solution?
  Divide Main Memory into pages, say 4KB each
  Divide Programs into pages (same size)
  Map Program Pages into Main Memory Pages
  Store extra Program Pages on disk
Main
Mem
Vista
IE
IE
IE

## Slide 78: Solution: Virtual Memory
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
e
s
D
i
s
k
a
d
d
r
e
s
s
e
s
V
i
r
t
u
a
l
a
d
d
r
e
s
s
e
s
A
d
d
r
e
s
s
t
r
a
n
s
l
a
t
i
o
n
IE
IE
IE
IE
IE
IE
IE
IE
IE sees this
Main Memory sees this
Can store some on disk!
Pages
Fragmented:
Non-contiguous (holes), out-of-order, some on disk
IE

## Slide 79: Address Translation
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
3
1
3
0
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
T
r
a
n
s
l
a
t
i
o
n
Table Lookup
Page Size: 2^12 = 4096 bytes
LDR R1, [R2, #8]

## Slide 80: Virtual Memory
Program Viewpoint
  Addresses start at 0
  Malloc() gives program contiguous memory (consecutive addresses)
  Malloc(), Free(), Malloc(), Free()
    Can malloc() re-use parts that are freed?
    Causes internal fragmentation within one program
  There is lots of free memory available
CPU/OS Viewpoint
  Keep all programs separate
    Don’t all start at 0
    Security implications…. programs should not read each other’s data!
  Dynamic program behavior causes memory fragmentation
    Starting & ending programs, swapping to disk
    Causes external fragmentation between programs
    Mitigated by virtual memory.
  Limited memory available
    Use Disk to hold extra data
    Use Main Memory like a cache for the program data stored on disk
New structure: Page Table

## Slide 81: Page Table: Big Lookup Table
D
i
s
k
a
d
d
r
e
s
s
e
s
IE
IE
IE
IE
IE
IE
IE
IE
Firefox sees this
Main Memory sees this
Fragmented:
Non-contiguous (holes), out-of-order, some on disk
Page Table
Virtual Addresses
Physical Addresses
Address Translation
IE
Pages

## Slide 82: Page Table
Holds virtual-to-physical address translations
Access like a memory
  Input: Virtual Address
    Only need Virtual PageNumber portion (upper bits)
    Lower bits are PageOffset, ie which byte inside the page
  Output: Physical Address
    Lookup gives a Physical PageNumber
    Combine with PageOffset to form entire Physical Address
Where to hold the PageTable for a program?
  Dedicated memory inside CPU? Too big! not done!
  Instead, store it in main memory

## Slide 83: Page Table Translation Structure
Size of Page Table?
2^20 or ~1 million entries
1 Page Table Per Program
Page Table Register
2
0
1
2
1
8
3
1
3
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
Virtual Address
Page Offset
Virtual Page Number
Physical Page Number
Physical Address
Physical Page Number
Page Offset
Page Table
Valid
If 0 then page is on disk

## Slide 84: Page tables may not fit in memory!
A table for 4KB pages for a 32-bit address space has 1M entries
Each process needs its own address space!
P1 index
P2 index
Page Offset
31
12
11
0
21
22
32 bit virtual address
Top-level table wired in main memory
Subset of 1024 second-level tables in main memory; rest are on disk or unallocated
Two-level Page Tables
1K
PDEs
1K
PTEs

## Slide 85: Page Table Implications
CPU executes “Load” instruction
  Recall: address is now a Virtual Address
  First step: Lookup address translation
    Where is page table? In main memory
    Special CPU register called Page Table Register (PTR)
      Holds starting address of page table
    Read DataMem from PTR+PageNumber to get Physical Address
  Second step: Access the data
    Read DataMem from Physical Address
Every load/store requires TWO memory accesses
  Slow!
  Can we speed up the translation step? Yes, use a cache!

## Slide 86: TLB: Translation Looksaside Buffer (A special cache for the Page Table)
1
1
1
1
0
1
1
0
1
1
0
1
1
1
1
1
0
1
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
TLB
Page Table
Tag
Physical Page Number
V
V
Physical Page Number or Disk Address
Physical Memory
Disk

## Slide 87: What about writes? How to determine what to put on disk?

## Slide 88: Memory Access:TLB Usage Algorithm
Both hardware and software solutions are possible for TLB miss
NOTICE: software designates some memory pages as READ-ONLY
Example: pages holding instructions.
It will may share some read-only pages with multiple programs, eg you run Firefox twice.

## Slide 89: TLB Notes
TLB Miss
  If handled by software: raises exception on TLB miss.
  If handled by hardware: special hardware unit will check DRAM for translation
  If page is not in DRAM, then need OS to transfer it in (“page fault”).
  OS handles security issues (invalidating TLB entries, etc…)
Read-only pages
  Can share non-sensitive data, eg instructions and pre-compiled data tables in a program such as Firefox
  Writes to read-only pages cause exception
  OS handles, possible outcomes:
    Illegal to write to this page
    Change page to writable
    If page is shared, make a new writable copy of this page for this program only. Remaining program share the original read-only copy. This is called “copy on write”

## Slide 90: Combined TLB & Cache Structure
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
1. TLB lookup
3. Access data cache
2. Convert VA to PA
NOTE: TLB is now slowing our cache!!

## Slide 91: TLB first, Cache second ?
TLB first, Cache second strategy is slow
  Called Physically Indexed, Physically Tagged
To improve performance:
  Lookup TLB, Lookup Cache at same time
  Must use Virtual Address to lookup in cache
  Compare Physical Address (output of TLB) to TAG (output of cache) when checking cache hit
  If OK, we can use the data
  Called Virtually Indexed, Physically Tagged

## Slide 92: Fast hits by Avoiding Address Translation
CPU
TB
$
MEM
VA
PA
PA
Naive
Organization
CPU
$
TB
MEM
VA
VA
PA
Virtually Addressed Cache?
CPU
$
TB
MEM
VA
PA
Tags
PA
Overlap $ access
with VA translation:
requires $ index to
remain invariant
across translation
VA
Tags
L2 $

## Slide 93: Why not just use virtual addresses for cache?
Substantial overhead to flush cache on context switch (dirty lines need to be written to memory if using writeback cache)
“cold start misses” resulting from flushing cache (increasing cache capacity does not help)

## Slide 94: Summary
Caches improve performance by giving the appearance of a very fast and very large memory.
Different cache designs: Fully associative, direct mapped, set associative. Replacement policies, cache write policies
Performance impact.
Virtual memory motivation; optimization of virtual memory using TLBs

## Slide 95: CPEN 211: In the beginning…