## Slide 1: CPEN 211: Computer Systems I Slide Set 1: The Digital Abstraction Combinational Logic
Prof. Tor Aamodt
By Unknown - U.S. Army Photo, Public Domain, https://commons.wikimedia.org/w/index.php?curid=55124
Notes: 0.5

## Slide 2: Learning Objectives
By the end of these slides, you should be able to:
Explain how noise motivates the use of digital signals in computing systems
Explain how digital values are encoded as voltages
Evaluate the impact of noise on a digital system.
Describe how binary values can be used to encode different types of information.
Define combinational logic and explain how to build larger combinational logic circuits out of smaller combinational logic circuits
Apply boolean logic to simplify logical expressions
Notes: 1

## Slide 3: Today, almost all electronics represents information digitally (e.g., using 0’s and 1’s). Why?

## Slide 4: Differential Analyzer (c. 1942)

## Slide 5: More Analog Computers…
Norden bombsight [Computer History Museum]
Notes: 1

## Slide 7: Thermostat Example
[http://blogs.plos.org/obesitypanacea/2011/02/25/turn-down-your-thermostat-to-lose-weight-suggests-new-study-dripping-with-sarcasm/]
[http://www.clipartpanda.com/categories/cute-house-clipart]
Next few slides consider an analog thermostat. We will see how noise impacts this design.

## Slide 8: Thermostat Controller
Text: Dally §1.4
The block labeled “Temp Sensor” senses the temperature in the room.
The arrow labeled “CurrentTemp” is the current temperature measured by the temperature sensor. “PresetTemp” is the temperature the room occupant desires. The block labeled “Compare A>B” compares CurrentTemp and PresentTemp and turns on the fan if the temperature in the room is too hot.
Here is one possible design:
Notes: 1.5

## Slide 9
Problem
Devices (electrons)
Getting electrons to solve problems…
?
Notes: 3
Slide courtesy: Prof. Yale Patt, Univ. of Texas at Austin
Problem: Compute list of suggested friends on facebook
Algorithm: Search social graph
Program: Algorithm to perform search… operating system you run the program on (Linux)
ISA: x86-64-bit
Microarchitecture: Pipelined, superscalar, out-of-order and speculative execution
Circuits: AND, OR, NOT; Half-adder, priority encoder, flip-flops, counters, registers, SRAM, DRAM, etc…
Electronic Devices: fin-FET CMOS

## Slide 10
Electrons accelerated by electric field.
Electric field generated by voltage differences.
[By Fir0002 - Own work, GFDL 1.2, https://commons.wikimedia.org/w/index.php?curid=2380067]
Notes: 1.5

## Slide 11: How to turn problem into voltages?
Analog approach: Use voltage to directly encode information
Example: Voltage = 0.2(Temperature − 68)
72.5 °F represented by …?
Text: Dally §1.2
Notes: 1
Need to process, transport and store information.

## Slide 12: Fun Fact: Thermal Noise
Resistor image: By oomlout (RESE-W04-X-O331-01) [CC BY-SA 2.0 (http://creativecommons.org/licenses/by-sa/2.0)], via Wikimedia Commons from Wikimedia Commons
Circuit Image: By Sbyrnes321 - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=28181783
You do NOT need
to know this
formula 
All wires have some resistance so they will have some amount of “noise”.

## Slide 13: Effect of Noise on Temperature Sensor Output
V
Input
+
e
Noise
V+
e
f
Output
E.g., disturb temperature by ε=100mV, new temperature signal is 1V which corresponds to 73 degrees instead of 72.5
Text: Dally §1.2
Time
Voltage
✘
Notes: 2
E.g., disturb temperature by 100mV, new temperature is 1V which corresponds to 73 degrees instead of 72.5

## Slide 14: Effect of Noise on an Analog System
Input (voltage) x
Output (voltage) f(x)
Consider a device that reads a voltage “x” at its input and outputs a voltage that is some function y=f(x). How it does that is not important.

## Slide 15: Effect of Noise on an Analog System
V
Input
+
e
Noise
V+
e
f
f(V+
e)
Output
Noise added to Input
Error at Output
Text: Dally §1.2
Time
Voltage
x
y
f(x) = 2x
(input)
(output)
Notes: 2
E.g., disturb temperature by 100mV, new temperature is 1V which corresponds to 73 degrees instead of 72.5

## Slide 16: Digital Binary
Alternative to Analog: detect presence or absence of a voltage – i.e., digital binary.
Typically, binary (0 or 1) values. Higher voltage means ‘1’ (“true”) low voltage means ‘0’ (“false”)
E.g., connect bulb to 120V, light turns on (“1”)
[By I, Funpika, CC BY-SA 3.0 us, https://commons.wikimedia.org/w/index.php?curid=2336969]

## Slide 17: Effect of Noise on Digital Signals
V
1
Input
+
e
Noise
V
1
+
e
f
f(V
1
)
Output
Text: Dally §1.2
Time
Voltage
Time
Voltage
x
y
f(x)
Restoration: Output is identical to Input despite
noise!
(input)
(output)
Simplest binary digital function “f”?
0 => 0
1 => 1
Notes: 1

## Slide 18: Effect of Nonlinear Function “f”
x
y
f(x)
V
1
+
e
Input + Noise
Time
Voltage

## Slide 19: Effect of Nonlinear Function “f”
x
y
f(x)
Time
Voltage
V
1
+
e
Output
Input + Noise
f(V
1
)
Why is this useful?
Small amount of noise leaves information unchanged. A low voltage is kept low and a high voltage is kept high.
Time
Voltage

## Slide 20: Buffer
Buffer
x
y
f(x)

## Slide 21: Avoiding Errors by “Going Digital”
Alternative to Analog: detect presence or absence of a voltage – i.e., digital binary.
Binary, meaning two, simpler than differentiating more than two voltages
Digital, meaning discrete, provides noise immunity.
Today’s systems move from analog to digital as soon as possible.
We will use positive logic: Higher voltage means ‘1’ (“true”) low voltage means ‘0’ (“false”)
Text: Dally §1.2
Notes: 2

## Slide 22: What is the impact of noise on large circuits?

## Slide 23: Impact on Large Circuits
Next consider impact of noise when there are multiple circuit elements.
We’ll look at both analog and digital systems.
We abstract the operation of each element to a simple function f(x)
For analog we examine linear function.
For digital we examine step function.
f(x)
f(x)
f(x)

## Slide 24
Noise
+
e
1
V
a
+
e
1
Noise
+
e
2
V
a
+
e
1
+e
2
V
a
Noise
+
e
3
V
a
+
e
1
+e
2
+e
3
The more analog circuits we combine the more noise accumulation impacts the output.
Text: Dally §1.2
Time
Voltage
Noise Accumulation

## Slide 25: “Beacon of Gondor” Buffer Analogy (Lord of the Rings)
Video: https://www.youtube.com/watch?v=i6LGJ7evrAg
“Gondor sends a signal to Rohan asking them for military aid”
[Analysis of fictional speed of propagation: http://scienceblogs.com/dotphysics/2010/07/30/how-fast-is-the-beacon-of-gond/ (photos above from this URL)]

## Slide 26: Signal Restoration
Noise
+
e
1
V
a
+
e
1
Noise
+
e
2
V
a
+
e
2
V
a
V
a
Noise
+
e
3
V
a
+
e
3
V
a
V
a
Restoration enables LARGE digital circuits to carry out complex, high-precision operations.
Text: Dally §1.2
Time
Voltage
Time
Voltage
Time
Voltage
Time
Voltage
x
y
f(x)
(input)
(output)
Notes: Here “a” is 0 or 1.
Digital systems process, transport, and store information without it being distorted by noise because they periodically *restore* a degraded 1 or 0 back to a clean 1 or 0 before an error accumulates and becomes larger than noise margin.

## Slide 27
Noise
+
e
1
V
a
+
e
1
Noise
+
e
2
V
a
+
e
2
V
a
V
a
Noise
+
e
3
V
a
+
e
3
V
a
V
a
Signal Restoration
Noise
+
e
1
V
a
+
e
1
Noise
+
e
2
V
a
+
e
1
+e
2
V
a
Noise
+
e
3
V
a
+
e
1
+e
2
+e
3
Restoration enables LARGE digital circuits to carry out complex, high-precision operations.
Buffer
Text: Dally §1.2
Time
Voltage
Time
Voltage
Time
Voltage
Noise Accumulation
x
y
f(x)
(input)
(output)

## Slide 28: How much noise can a digital circuit tolerate?

## Slide 29: Digital Logic - Requirements
Let’s revisit what we mean by “detecting the presence or absence of a voltage”.
In prior examples looked at “threshold function”.
Too simple to model real circuits as it includes portion with an infinite slope.
Different power supply voltages.
Leads to consideration of requirements that circuit elements must satisfy to be useful.
x
y
f(x)

## Slide 30: Signal Restoration
Buffer
x
y
f(x)
Buffer gets rid of noise. Getting rid of noise also called signal restoration.
The input/output operation of a circuit can be characterized using a curve known as the DC voltage transfer function.
For the ideal buffer DC voltage transfer function (shown at top left), logic values are represented by a set of voltage values. The set of voltage values used to represent a given logic value is different at input versus the output.
E.g., Suppose supply voltage was 5 V and threshold (input voltage value when output “jumps”) is 2.5 V. What voltages represent logic “0” and “1”?
Input: logic “0” represented by voltage below 2.5 V
Output: logic “0” represented by voltage equal to 0 V
Input: logic “1” represented by voltage above 2.5 V
Output: logic “1” represented by voltage equal to 5 V

## Slide 31: Characteristics of a “Buffer” Circuit
Buffer
x
y
f(x)
1. Logic values represented by input or output wire within a voltage range.
2. The voltage range used for a logic value is different at input and output.

## Slide 32
“0”
“1”
H
Slope > 1 here
To tolerate noise: H < W.
W
H
Slope > 1 means buffer “gain” must be greater than one. => Need “active” element.
“0”
“0”
“1”
“1”
H
W
“0”
“1”

## Slide 33
“0”
“1”
“0”
“0”
“1”
“1”
“0”
“1”

## Slide 34: Voltage Ranges of Binary Signals
0
1
?
Voltage
Damage
Damage
Vmin
V0
VIL
VIH
V1
Vmax
-0.3V
0.0V
0.7V
1.7V
2.5V
2.8V
2.5V LVCMOS Logic
Text: Dally §1.1
For example, 2.5V LVCMOS logic, all input voltages between Vmin=-0.3V and VIL = 0.7V represent logic value of “0”.
A “standard” set of voltages. Defined by an industry standards organization called JEDEC.
Notes: 1.5

## Slide 35: Noise Margin
Voltage
?
Damage
Damage
Vmin
V0
VIL
VIH
V1
Vmax
0
Tran
VOH
VOL
VNMH
VNML
Key to restoration: Output range for “1” narrower than input range for “1”. This provides noise margin.
Similarly, output range for “0” narrower than input range for “0”.
Text: Dally §1.2
0
Tran
Notes: 2

## Slide 36: Example (Supply Noise)
Two chips, A and B, use the 2.5V LVCMOS encoding to send logic signals from A to B:
Suppose there is a voltage shift between the two chip’s power supplies so that all voltages in A are VN higher in B.
2.5V LVCMOS
A
B

## Slide 37
A voltage of Vx in system A appears as a voltage of Vx + VN in system B. Assuming no other noise sources, what is the maximum value of VN for which the system operates properly?
VGND = 0V
VOL = 0.2V
Vdd = 2.5V
VOH = 2.1V
0
Tran
?
Damage
Damage
VN
Vmin = -0.3V
VIL = 0.7V
VIH = 1.7V
Vmax = 2.8V
VN
Chip A
Chip B
(a) Vdd+ VN <= Vmax AND
(b) VOL+ VN <= VIL
(a) 2.5V + VN <= 2.8V AND
(b) 0.2V + VN <= 0.7V
(a) VN <= 0.3V AND
(b) VN <= 0.5V
VN <= 0.3V

## Slide 38: Representing Information Beyond 0 and 1

## Slide 39: Representing Information
“What's in a name? that which we call a rose
By any other name would smell as sweet”
[William Shakespeare, Romeo and Juliet]
By gnuckx (A red rose for Elena - Creative Commons by gnuckx)
[CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)],
via Wikimedia Commons from Wikimedia Commons
Notes: Earlier we said we would represent “false” with a low voltage and “true” with a high voltage.
It is important to recognize that in some sense the choice of associating a low voltage or logic level 0 with “false” is arbitrary. It is not unlike associating the English word “rose” with the plant shown above. However, the choice can have an impact on how easy it is to operate on the information.
Another issue that arises with digital representations is the number of different things we can represent. For the picture on the left each pixel can only be black or white. For the picture on the right, each pixel can take on any one of millions of different colors.

## Slide 40: Representing Information
Earlier saw we could represent temperature with a voltage:
  Voltage = 0.2(Temperature − 68)
  0.9 V represents 72.5 °F
Also saw we could represent a binary value with a voltage:
  0 V represents “0”
  2.5 V represents “1”
Two separate things:
  The information we are interested in.
  The representation of that information.
Let’s consider how to represent information in binary…

## Slide 41
With 0 and 1 we can represent two things
A description is “True” or “False”
Door “open” or “closed”
light “on” or “off”
Text: Dally §1.3
Notes: 1.5

## Slide 42
Element of a set: E.g., colors
 | White
 | Red
 | Blue
 | Yellow
 | Purple
 | Orange
 | Green
 | Black
Text: Dally §1.3
Often deal with information that is NOT “binary”
With k “bits” we can represent at most 2k different things.
000 | 
001 | 
010 | 
011 | 
100 | 
101 | 
110 | 
111 | 

## Slide 43
Continuous Quantities: E.g., temperature
000 | 68
001 | 70
010 | 72
011 | 74
100 | 76
101 | 78
110 | 80
111 | 82
0000000 | 68
0000001 | 70
0000011 | 72
0000111 | 74
0001111 | 76
0011111 | 78
0111111 | 80
1111111 | 82
Text: Dally §1.3
Often deal with information that is not binary:
[http://blogs.plos.org/obesitypanacea/2011/02/25/turn-down-your-thermostat-to-lose-weight-suggests-new-study-dripping-with-sarcasm/]
Notes: 1

## Slide 44: We pick a binary representation (name) based on the operations required

## Slide 45: Example

## Slide 46
Pick representation of colors to support the operation of “subtractive” color mixing
  No colors - white
  Primary colors – red, blue, yellow
  Derived colors – orange, purple, green, black
How to represent individual colors if we want to efficiently compute result of combining colors?
000 | White
 | Red
 | Blue
 | Yellow
 | Purple
 | Orange
 | Green
 | Black
Text: Dally §1.3
001 | 
010 | 
100 | 
011 | 
101 | 
110 | 
111 | 
Binary
Encoding
Meaning
Binary
Encoding
Meaning
Notes: 2

## Slide 47: How would you represent
A Date ?
  Days since Jan 1 0000 (20 bits)
  Month, day, year (4 + 5 + 12 bits)
  Month, day, year, day of week (4 + 5 + 12 + 3 bits)
A playing card ?
  Number in deck (6 bits)
  Suit, Number (2 + 4 bits)
  Decoded suit, decoded number (4 + 13 bits)
A 5-card hand?
Text: Dally §1.3
Notes: 735,110 days ; 2^20 = 1,048,576
12 months, requires 4-bits (16)
31 days in month, requires 5-bits (32)
How many years? 11-bits 2048, 12-bits 4096

## Slide 48: Representing Numbers
Many ways to represent same value
E.g., number five can be written as “5”.
Hand with fingers+thumb extended.
Unary encoding: 11111 or . Used for counting birthdays (candles on cake).
Will see binary representation for five is 101
Will also see (in 2-3 weeks) floating-point
IMPORTANT: Digital logic always uses 0’s and 1’s. Decimal numbers in Verilog are converted to 0’s and 1’s by Quartus during synthesis.
Notes: 2

## Slide 49: Unsigned (non-negative) Integers
Unsigned integers useful for counting
Example 1: Track number of times we have completed a task.
Example 2: Identify different memory locations (e.g., 129 Main St. vs 131 Main St.)
Text: Dally §10.1
Notes: 1.5

## Slide 50: Unsigned Integers in Binary
Decimal: E.g., 329 = 3×102 + 2×101 + 9×100
binary digits are 0 and 1
E.g., with five bits, represent number 6 as 00110
This means 0×24 + 0×23 + 1×22 + 1×21 + 0×20
0×16 + 0×8 + 1×4 + 1×2 + 0×1
Text: Dally §10.1
Notes: 2

## Slide 51: Converting from Decimal to Binary
Expand, convert, evaluate (not recommended)
329 = 3×102 + 2×101 + 9×100
= 11×1100100 + 10×1010 + 1001x1
= 101001001
2. Division by 2 method
If least significant decimal digit is odd (even), then least significant binary digit is 1 (0).
329 (odd) => 1, 329 ÷ 2 =
164 (even) => 0, 164 ÷ 2 =
82 (even) => 0, 82 ÷ 2 =
41 (odd) => 1, …
Subtraction method (see text: Dally 10.1)
Text: Dally §10.1
Notes: 2.5

## Slide 52
[http://vlsiarch.eecs.harvard.edu/accelerators/die-photo-analysis]
Apple A8 die photo
(application processor
used in iPhone 6)

## Slide 53: Two Types of Digital Logic!
“Sequential Logic”
“Combinational Logic”
remembers things…
forgets things…

## Slide 54: Wires and busses
Both sequential and combinational logic are built using wires and busses.
Single wire carries one bit (e.g., 0 V or 2.5 V for “0” or “1”)
If we want to send N bits (e.g., to represent one of 2N temperatures) we need N wires. Often referred to as N-bit bus.
Ribbon cable with 20 wires.
I.e., a 20-bit bus.
20
Schematic symbol:
Notes: 1.5

## Slide 55: Combinational Logic Circuit
Present output is a function of present input
Past input values do NOT matter
Example – digital thermostat
Means this signal is 3-bits wide
Text: Dally §1.4
000 | 68
001 | 70
010 | 72
011 | 74
Notes: 1.5

## Slide 56: Recall: Functions
[http://2012books.lardbucket.org/books/beginning-algebra/s12-05-graphing-parabolas.html]
“x” is input
y is “output”

## Slide 57: Combinational logic implements a memoryless function
output = f(input)
Text: Dally §6.1
i1 i2 i3 | o1
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1
[http://2012books.lardbucket.org/books/beginning-algebra/s12-05-graphing-parabolas.html]
instead of “real” numbers
combinational logic
uses “binary"
input output
Notes: 1.5

## Slide 58
combination = R31-L23-R0
Current output (locked/unlocked) depends upon past inputs
Current output (locked/unlocked) depends
only on current inputs
Sequential Logic
Combinational Logic
Notes: 1.5

## Slide 59: Sequential logic circuits
Includes state (memory, storage)
Makes output a function of history as well as current inputs
Synchronous sequential logic uses a clock
Example: A calendar circuit that remembers current date and updates the date each morning.
Text: Dally §1.4
September = 910 = 10012
9th day = 910 = 10012
Wednesday = 3 = 0112
September = 910 = 10012
10th day = 1010 = 10102
Thursday = 4 = 1002
Notes: 2

## Slide 60: Building Larger Circuits

## Slide 61
[http://blogs.plos.org/obesitypanacea/2011/02/25/turn-down-your-thermostat-to-lose-weight-suggests-new-study-dripping-with-sarcasm/]
[http://www.clipartpanda.com/categories/cute-house-clipart]

## Slide 62: Can compose digital circuits
Text: Dally §1.4
Notes: 2
Suppose we want to modify our thermostat so that the fan does not run on Sundays.
Important part of digital design is partitioning up a design into smaller portions. In 259 we study in detail an example which is the digital system inside a computer.

## Slide 63: Closure
(Set Theory) Combinational logic circuits are “closed” under “acyclic composition”
In plain English: If we combine two combinational logic circuits without introducing a cycle, the resulting circuit will also be combinational.
CL1
CL2
CL12
Text: Dally §6.2
Notes: 1.5

## Slide 64
Text: Dally §6.2
Notes: 1

## Slide 65: How to design combinational logic?

## Slide 66: Google Tensor Processing Unit (TPU)
[Image Source: https://cloudplatform.googleblog.com/2016/05/Google-supercharges-machine-learning-tasks-with-custom-chip.html]

## Slide 67: Deep Learning: Where Times Goes
~ 90% of time  dot products
X
X
+
100s
-
1000s
More details: http://www.ece.ubc.ca/~aamodt/papers/Cnvlutin.ISCA2016.pdf

## Slide 68: Design Steps
Describe desired functionality (e.g., Verilog)
Minimize cost of implementation (e.g., Quartus)

## Slide 69: Several ways to describe a combinational logic function
Example – “Majority Circuit”
English Language Description
  Outputs 1 if more inputs are 1 than are 0
Truth table
Logic equation (Boolean algebra)
  q = (a b)  (a  c)  (b  c)
abc | q
000 | 0
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 1
Notes: 2

## Slide 70: Why Boolean Algebra?
If a truth table can completely describe a combinational logic function, why do we need logic equations and Boolean algebra?
Two reasons:
  Easy to convert from a logic equation to circuit
  We can use the “laws of Boolean algebra” to simplify the circuit to save cost

## Slide 71: Several ways to describe a combinational logic function
Logic gate diagram
Verilog
assign f = (a&b)|(a&c)|(b&c);

## Slide 72: Boolean Algebra
“high school” Algebra:
  Algebra over infinite set – e.g., real numbers (-, )
  4 operators: Multiplication (*), addition (+), subtraction (-), division ()
Boolean Algebra:
  algebra over 2 element set: {0,1}
  3 operators: AND (), OR (), NOT ()
Text: Dally §3 (1st page intro)
Notes: 1.5

## Slide 73: Boolean Algebra
AND Operation (“conjunction”)
  Definition: a  b = 1 if and only if a=1 and b=1
  Similar to English definition of “and”.
OR Operation (“disjunction”)
  Definition: a  b = 1 if a=1 or b=1
  Similar to English definition of “or” but note that a  b is “1” when both a=1 and b=1.
NOT Operation (also called “complement”)
  Definition: a = 1 iff a=0
  Other notations: a = a’ = a
Text: Dally §3 (1st page intro)
Notes: “NOT a” can also be written as a with a bar over it or a’

## Slide 74: Boolean Algebra
Truth tables defining AND, OR and NOT:
a | b | a^b | a v b
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1
a | ~a
0 | 1
1 | 0
Text: Dally §3 (1st page intro)
Notes: 1.5

## Slide 75: Note on Notation
For AND logic function:
  use 
  don’t use x nor .
For OR logic function:
  use 
  don’t use +
This avoids confusion between Boolean algebraic rules and rules of “normal” arithmetic.
Text: Dally §3 (1st page intro)
Notes: 1.5

## Slide 76: Axioms of Boolean Algebra
Axioms: a set of mathematical statements that we assert to be true.
Annihilation:
  0  x = 0
  1  x = 1
Identity:
  1  x = x
  0  x = x
Negation:
  0 = 1
  1 = 0
Text: Dally §3.1
Notes: 2

## Slide 77: Example: Absorption
Prove that x  (x  y) = x by using perfect induction (i.e., enumerate all the possibilities).
(We will fill this in during class)

## Slide 78: Example: DeMorgan’s Law
Prove that (x  y) = x  y by using perfect induction (i.e., enumerate all the possibilities).
x | y | x  y | (x  y) | x | y | x  y
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0
Text: Dally §3.2
Notes: 1.5

## Slide 79: Principle of Duality
If a Boolean equation is true, then substituting  for each ,  for each , 1 for each 0, and a 0 for each 1 results in an equation that is also true.
Since it holds for axioms (dual of “0  x = 0” is “1  x = 1” which is also an axiom) it also holds for rest of Boolean algebra.
Text: Dally §3.1
Notes: 1.5

## Slide 80: Dual Functions
Dual of logic function f, is function fD derived from f by substituting a  for each , a  for each , a 1 for each 0, and a 0 for each 1.
Useful property for understanding CMOS gates: dual of a function applied to the complement of the input variables equals the complement of the function.
Text: Dally §3.3
Notes: 1

## Slide 81: Example of
f(x,y) = (x  1)  (0   y)
fD(x,y) = (x  0)  (1   y)
fD( x,  y) = ( x  0)  (1  y)
x | y | (x  1) | (0  y) | f(x,y) | f(x,y) | (x  0) | (1  y) | fD(x, y)
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0

## Slide 82: Useful Boolean Properties
Communicative | x  y = y  x | x  y = y  x
Associative | x  (y  z) = (x  y)  z | x  (y  z) = (x  y)  z
Distributive | x  (y  z) = (x  y)  (x  z) | x  (y  z) = (x  y)  (x  z)
Idempotence | x  x = x | x  x = x
Absorption | x  (x  y) = x | x  (x  y) = x
Combining | (x  y)  (x  y) = x | (x  y)  (x  y) = x
DeMorgan’s | (x  y) = x  y | (x  y) = x  y
Text: Dally §3.2
Highlighted = different relations than for + and ✕ with real numbers
All properties below can be derived from the axioms.
Useful for simplifying Boolean expressions to use less operations => reduce cost.
Notes: 2

## Slide 83: Example
Reduce the following Boolean expression to a minimum number of literals:
f(a,b,c) = (a  c)  (a  b  c)  (a  b  c)  (a  b  c)

## Slide 84: Normal Form (From Truth Table to Equations)
Can also compare Boolean expressions for equality by reducing to a normal form.
Two types of normal form: sum of product, product of sums
A product term is boolean expression with any number of inputs or their complement AND’ed together. E.g., a  b.
In sum of products normal form each product term corresponds to single row in truth table with a ‘1’ output.
Input variable complemented if zero in truth table.
Normal form => products in same order as in truth table.
E.g., for majority circuit:
abc | q
000 | 0
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 1
Text: Dally §3.4
Notes: 3

## Slide 85: Example
Rewrite the following Boolean expression in normal form: f(x, y, z) = 1 if exactly 0 or 2 inputs are 1.
xyz | f
000 | 
001 | 
010 | 
011 | 
100 | 
101 | 
110 | 
111 | 

## Slide 86: Factoring Functions
Recall we can “factor real” valued functions. You might have done examples such:
[above example from: https://www.symbolab.com/solver/factor-calculator]

## Slide 87: Shannon Expansion
Turns out we can also factor Boolean functions. Can do so systematically using a process called Shannon Expansion.
Select an input and re-write function as disjunction () of two products: The first is the conjunction () of the selected input with the function evaluated with that input set to 1; the second is the conjunction () of the selected input inverted with the function evaluated with that input set to 0.
Example, expand F “around” input :

## Slide 88: Example: Prime Function
Can factor any Boolean function of n-inputs:
For prime function (F=1 if is prime or 1):
Expand around
Repeating for other two inputs will lead to the sum-of-products normal form.

## Slide 89: Summary
The world is digital
  Systems are digital at their core, only analog on the edges
Representing information
  Binary signals, sets, continuous values
Digital signals reject noise
  Voltage range divided into discrete states
  Noise margins
Combinational logic
  Output depends only on input (no state)
Boolean algebra
  Rules to manipulate logic equations