## Slide 1: CPEN 211: Computer Systems I Slide Set 3: Combinational Logic Optimization (Flipped Lecture)
Instructor: Prof. Tor Aamodt
WARNING: Be sure to complete the online portion of Flipped Lecture #1
before the start of lecture on Thu 19 Sep 2024 or you will lose marks.
Notes: Welcome to the first flipped lecture for CPEN 211 at UBC. In this lecture we will discuss logic optimization building upon your knowledge of logic gates from Slide Set 2.

## Slide 2
Sequential App Performance
Notes: This figure shows several important technology trends related to digital systems design. The top red line in the figure shows the growth in number of transistors integrated into a single chip on the y-axis versus year on the x-axis. As you can see back in the 1970’s a single chip could contain on the order of 100 transistors. Today in 2015 the many chips integrate several billion transistors.

## Slide 3
Exponential growth in number of transistors per chip (Moore’s Law).
This growth far outpaces the number of engineers per design team.
Implications of this?
Notes: This exponential growth in number of transistors per chip is known as Moore’s Law.
Note that this growth in the number of transistors we can implement on a single chip far outpaces the number of engineers per design team.
What are the implications of this?
Well, one is that if engineers had to directly apply Boolean optimization using the techniques in Slide Set 1 and 2 it would take far too long to design such a chip even with thousands of engineers. Instead, engineers specify a design using a language such as Verilog, which is then input to a software tool that automatically generates the low level design. However, to become an effective designer using Verilog it is necessary to have some understanding of how these tools work internally. This is the motivation for learning the material in this lecture.
Another observation, is that while transistors are now very cheap, there is a limit to how many transistors we can build on a chip. Hence, we would like to use as few transistors as possible for a given application.

## Slide 4: Introduction
In this slide set we look at how to reduce number of gates used in a circuit without changing that circuit’s behavior.
Generally, we let the CAD tools do this for us, but good to understand how they work (what they are capable of and what they are not).
First, we consider several ways of representing combinational logic functions
Text: Dally §6
Notes: In this slide set we will look at how to reduce the number of gates used in a circuit without changing it behavior.
As just noted, generally we let the CAD tools such as Quartus that you use in the labs, do this for us. By understanding how a tool like Quartus works internally, you will have a better idea of what matters and what does not matter when writing your Verilog.
Before discussing this process of optimizing the implementation of logic functions, we will start by considering several ways of representing combinational logic functions.

## Slide 5: Learning Objectives
By the end of this slide set you should be able to:
Translate a word description of a logic function into a truth table
Define terminology related to logic optimization
Explain algebraic simplification using Cube representation of logic function
Reduce gates for sum-of-products or product-of-sums normal form using a Karnaugh Map for both completely and incompletely specified functions
Eliminate hazards in combinational logic

## Slide 6: English language description of a combinational logic function
F(d,c,b,a) is true if input d,c,b,a is prime
Notes: Let’s start by considering an example of how we might specify a design in English. We will return to the design in this example several times throughout this lecture.
In this example we are interested in prime numbers, that is, numbers that are only divisible by themselves and the number 1. Examples are 2, 3, 5 and 7. We can specify this design using the following English statement.
F(d,c,b,a) is true if the input d,c,b,a taken together as a 4-bit number, is prime.
We can specify this same design in other ways.

## Slide 7: Truth Table
F(d,c,b,a) is true if input d,c,b,a is prime
Note there is some redundancy in truth table - we could simply list rows with a ‘1’ output
Text: Dally §6.3
Truth table representation is unique.
Notes: For example, we could also specify this design using a truth table as follows. Here each row specifies the output of the circuit for a particular combination of inputs. The input bits are listed in order in the first set of columns and the output is in the right hand column. For example, the number three as a four bit binary number is 0011, which is in this row here. Since three is a prime number the output is 1 in this row. The number four in binary is 0100, which is listed in the next row. As four is not a prime number, the output listed for it is zero.
What is the output q when the input is 1100?
The answer is A, zero. As we can see here, the row with input dcba equal to 1100 has output q equal to 0. Let’s make sure this is consistent with the desired functionality. We want the output to be 1 when the input is a prime number. 12 is the product of 3 times 4, so it is not a prime number. So, it makes sense the output is 0 for input 1100.
One thing to observe is that the truth table representation of a logic function is unique.
Also, note there is some redundancy in truth table - we could simply list rows with a ‘1’ output. We can eliminate this redundancy and achieve a smaller table using what is known as an abbreviated truth table.

## Slide 8: Abbreviated Truth Table
List only rows that have ‘1’ output.
F(d,c,b,a) is true if input d,c,b,a is prime
Text: Dally §6.3
Notes: The abbreviated truth table is like a regular truth table except that we omit rows for which the output is zero. I.e., we list only rows that have ‘1’ output. The next question we want to consider is “how to turn this specification into a circuit built out of AND, OR and NOT gates?” Initially, we will not worry at all about whether the circuit is optimized. We just want to convert this table into a circuit that correctly implements the function specified in the abbreviated truth table.

## Slide 9: Example:
Notes: First, let us consider a simple example. How would we convert the logic function “A and NOT B” into a circuit?
We can use the approach described at the end of Slide Set 2 to directly draw the following schematic from the Boolean expression.

## Slide 10: Example:
Only true if A is true and B is false
A | B | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
A | B | f
1 | 0 | 1
Truth Table
Abbreviated Truth Table
f
Notes: Now consider the truth table for this simple function. First, note that the expression “A and NOT B” is true ONLY when A is true and B is false. I.e., “A and NOT B” is true when A has a logic value of 1 and B has a logic value of zero.
Here is the truth table representation for this function. As we can see there is only one row for which the output is 1. For all other rows the output is zero. The reason only one row has an output of 1 is that we are using AND. You could say the AND gate is very particular and only “happy”, when ALL of its inputs are true.
Given there is only one row in the truth table that has an output of 1, the abbreviated truth table contains only a single row.
Compare the circuit we drew previously for this logic expression to the entries on the input side of this single row. Notice how input B in the abbreviated truth table is zero and in the circuit diagram it is first fed into a NOT gate which then connects to the AND gate. In contrast the input A in the abbreviated truth table is one and in the circuit diagram it is fed directly into the AND gate.
This is not coincidence. In general, we can directly convert from the abbreviated truth table to a logic diagram by considering each row one by one. Each row will get its own AND gate with as many inputs as there are inputs in the truth table. Each input that is 1 in that row is directly connected to the AND gate. Each input that is 0 is first passed through an inverter.

## Slide 11: Schematic Logic Diagram
Abbreviated truth table:
Notes: Using the insights from the prior example let’s convert the abbreviated truth table for the prime number function into a digital circuit. In the first row we have 0001. We translate this into a four input AND gate.
As the inputs d, c, and b are all zero these inputs are first connected to NOT gates and then the output of those NOT gates is connected to the AND gate.
The input a is 1 so we connect it directly to the AND gate without a NOT gate.
Recall that the output of an AND gate is 1 only when all inputs are 1 as this is the definition of an AND gate. What happens when dcba=0001?
As the input to each NOT gate is zero, the output of each NOT gate is one.
Thus all inputs to the AND gate are all 1 and so the output value will also be 1.
What happens for any other input value of dcba? If we change a from 1 to 0
then one of the inputs to the AND gate is zero so the output of the AND gate will be zero.
What happens if we had instead changed d from 0 to 1? Let’s first put the value of a back to 1.
Changing the value of d fed into the NOT gate causes the output of the NOT gate to go from 1 to 0. Again we have one of the inputs to the AND gate is zero so the output of the AND gate is zero.
Only when the value of d is 0, the value of c is 0, the value of b is zero and the value of a is 1.
Next, let’s consider the next row in the abbreviated truth table, 0010. We first draw the AND gate.
To keep our logic diagrams more compact, we will simply draw a bubble where we want a NOT gate. As inputs d, c and a are zero we first connect these to NOT gates. Only input b is connected directly to the AND gate.
Notice the output of this AND gate is only true when input d is 0, c is 0, b is 1 and a is zero.
Notice we now have a circuit with two outputs. The first one represents the first row in the abbreviated truth table and the second one represents the second row in the abbreviated truth table. However, our prime number function is supposed to only have a single output. Moreover the output should be 1 for any input combination in the abbreviated truth table. In other words the output is true when the output of the first AND gate is 1 OR the output of the second AND gate is 1. We can implement this by simply adding an OR gate that is connected to the outputs of each AND gate.

## Slide 12: Schematic Logic Diagram
Each AND gate represents one row in abbreviated truth table.
Schematic Logic Diagram:
Abbreviated truth table:
0 1 0 1
0
0
0
1
0
0
0
1
Text: Dally §6.3
Notes: Continuing in this way we obtain the following picture.
Again, each AND gate represents one row in the abbreviated truth table.
The corresponding Boolean expression has all four inputs to the function ANDed together. If that input is zero in the truth table it is complemented with a NOT gate. We represent that with a bar over the input in the logic expression.
Let’s consider the operation of this circuit for different inputs.
First, consider the input 0101.
What is the output of the first AND gate corresponding to row 1 in the abbreviated truth table, when this is the input?
The answer is zero. For the input dcba=0101, the logic expression corresponding to the first AND gate evaluates to zero as shown here.
For the same input, what is the output of the second AND gate corresponding to row 2?
The answer is zero.
What is the output of the AND gate corresponding to row 3?
The answer is zero.
What is the output of the AND gate corresponding to row 5?
The answer is 1.
Continuing in the same way the final three AND gate outputs are zero. Notice that the output of only one AND gate is true.
The outputs of the seven AND gates are feed into a seven input OR gate. Recall that the function of an OR gate is defined such that the output is one whenever any of the inputs are one. As the fourth input is one, the output of the OR gate is one.
Does this make sense? The input 0101 corresponds to the number five which is a prime number. So our circuit is working as expected for this input. You may want to test other inputs to verify the output of the circuit is one only for prime numbers. For example, you might want to try seeing what happens when the input is four or 0100 in binary.
This circuit represents the prime number function using two levels of logic. The first level includes all the AND gates. The second level is the seven input OR gate. This form is often called “sum of products normal form”. Any combinational logic function can be implemented using such a two level form by similarly transforming it’s truth table representation into AND, OR and NOT gates.
This circuit correctly implements the desired function. However, it is not a very efficient representation. It requires seven four input AND gates a seven input OR gate and a large number of NOT gates. Shortly we will see how to optimize the circuit to reduce the number of gates.

## Slide 13: Equation
row numbers in abbreviated truth table
Sum of products normal form.
As with truth table, unique.
Text: Dally §6.3
Notes: The sum of products normal form can be represented even more compactly as an equation using the following notation. We simply write a capital sigma, meaning sum, and then a lowercase “m” followed by a comma separated list of the row numbers from the abbreviated truth table.
As with the truth table, the sum of products equation form is unique.

## Slide 14: Logic Optimization
Would like to implement same logic function using fewer logic gates
E.g., want to implement prime number function using as few AND, OR, NOT gates as possible.
We will restrict ourselves to considering two-level logic implementations.
Notes: The goal of logic optimization is to implement the same logic function using as few logic gates as we can.
For example, we would like to find a way to build a circuit implementing the prime number function using as few AND, OR, and NOT gates as possible. In Slide Set 1 we saw an example of how to use Boolean properties to simplify a Boolean expression. However, it was unclear which order to apply these rules. We want a systematic approach to finding a good order to apply the Boolean properties such that we end up simplifying a given Boolean logic expression.
For simplicity, we will restrict ourselves to considering two-level logic implementations.

## Slide 15: Observation
Some rows of abbreviated truth table differ only in one position of input “dcba”.
E.g., row 0010 and 0011 differ only for least significant (rightmost) bit.
Text: Dally §6.4
Notes: To start, observe that some rows in the abbreviated truth table differ in only one input bit position.
For example, row 0010 and row 0011 differ only for the least significant (i.e., rightmost) bit corresponding to input a. For these two rows, whenever dcb is 001 the output is 1 regardless of whether input a is 0 or 1.

## Slide 16
“combining rule”:
(p  q)  (p  q) = p
Product term contains only 3 of 4 input variables
If bits of dcba can be “X” (match 0 or 1) can replace these two rows with a single row 001X.
Text: Dally §6.4
Notes: For these specific two rows, we could reduce the size of our truth table if we could write a single row to represent both rows of the abbreviated truth table.
To do this we introduce a symbol X that indicates a match to either a zero or a one. Specifically, if bits of dcba can be “X” which means match 0 or 1, then we can replace these two rows with a single row 001X. This single row will require fewer gates to implement.
The combining of rows is actually an application of the “Combining” rule, which was one of the useful Boolean properties listed in Slide Set 1. The combining rule says that if we OR together two product terms where the two product terms differ in only one position and the difference is that an input appears complemented in one product term and uncomplemented in the other, then we can eliminate that input. Here, q is complemented in the first product term and uncomplemented in the second so we can eliminate it and end up with just p.
This Boolean expression represents the two highlighted rows.
Notice the first three literals in the first product term match the first three literals in the second product term.
The last literal in the first product term
is the complement of the last literal in the second product term.
Hence, if we equate the first three literals with p and the last literal with q in the combining rule, we see we can eliminate one of the four inputs from the expression along with one of the product terms.
The resulting single product term contains only 3 of 4 input variables.

## Slide 17: 001X
Before applying “Combining Rule”
After applying “Combining Rule”
Notes: What is the effect of combining two rows in the abbreviated truth table on the size of the logic circuit?
Before combining, the two rows could be implemented with the following circuit.
The result after applying the combining rule much smaller than what we started with.

## Slide 18: To reduce hardware cost, we need a systematic method to identify rows of truth table with output ‘1’ that differ by only one input variable
Notes: So, to find a good order to apply the combining rule what we need is a systematic method to identify rows of truth table with output ‘1’ that differ by only one input variable.
The technique we will learn to do this later in this lecture is a table based approach known as the Karnaugh Map or KMAP method. It was developed around 1952 at Bell Labs and is still useful for providing intuition into logic optimization. Before we can get to the KMAP technique, we need to introduce some terminology.

## Slide 19: Minterms
A minterm is a product term that includes each input of a circuit or its complement. Represents one row in truth table (the minimum number).
For a boolean function of N variables there are 2N rows in truth table and 2N minterms.
For example, is a minterm for prime.
Text: Dally §6.4
Notes: A Minterm is a product term that includes each input of a circuit or its complement. It represents one row in the truth table -- the minimum number.
For a Boolean function of N variables there are 2^N rows in the truth table and 2^N minterms.
For example, “NOT d AND c AND NOT b AND NOT a” is a minterm for prime.
Is “¬ d  ¬ c  b” a minterm for the 4-input prime function with inputs d, c, b, a?
The answer is no. The reason is this expression includes only 3 out of the 4 inputs.

## Slide 20: Implicants
A product term that is true only when a boolean function is true is called an implicant of that function.
When the product term is true that fact implies the function is also true.
For example, and are both implicants of the prime number function.
Text: Dally §6.4
Notes: A product term that is true only when a Boolean function is true is called an implicant of that function.
When the product term is true that fact implies the function is also true.
For example, “NOT d AND NOT c AND b” is an implicant of the prime number function and so is “NOT d AND NOT c AND b AND NOT a”.

## Slide 21: Implicants vs. Minterms
Minterm is implicant only if corresponds to a row with ‘1’ output in truth table.
A “minterm of a function” is both a minterm and an implicant.
Text: Dally §6.4
Notes: A minterm is an implicant only if it corresponds to a row with an ‘1’ output in the truth table.
For example, “NOT d AND NOT c AND b AND NOT a” is an implicant because it is a minterm that corresponds to a row for which the output is 1.
A “minterm of a function” is both a minterm and an implicant.
In the sum of products form the little “m” stands for “minterm of the function”.

## Slide 22: Cube representation (3-bit prime)
å
=
cba
m
f
)
7
,
5
,
3
,
2
,
1
(
Adjacent vertices on cube differ in only one input variable.
Each vertex of cube corresponds to a minterm
Focus on vertices that correspond to minterms that are implicants
Text: Dally §6.4
Notes: Now that we have defined some key terminology we can take our first step towards learning the KMAP method. Note that the following discussion may seem a little bit abstract but it is key to understanding why the KMAP technique works. We want you to understand why the KMAP technique works for a few reasons: First, so that you know how to correctly apply it. second, so you can recall it more easily; third, to help develop your intuition for digital logic design.
First, we consider a simpler prime function with three inputs. The output for this function is one if the input is 1, 2, 3, 5 or 7.
We will visualize each minterm in the truth table as a vertex of a cube. For example, the bottom left corner represents the row in the truth table with all inputs equal to zero. Each dimension of the cube corresponds to an input variable. Horizontally, the input a changes going from 0 to 1 from left to right. Into the screen, the input b changes. Vertically, the input c changes.
What input variables change between the two vertices circled in blue?
The answer is c. Notice that c is 1 for the top vertex and 0 for the bottom vertex. Let us consider the Boolean expressions corresponding to these two vertices. Notice these differ in only one position corresponding to the input c.
Now, let us focus on vertices that correspond to minterms that are implicants. These are highlighted on the right in red. The highlighted vertices each correspond to an individual row of the abbreviated truth table. Moreover, highlighted vertices that are connected by an edge correspond to rows that differ in only a single input being complemented for one vertex versus the other. Let us focus on one such edge.

## Slide 23: Cube representation (3-bit prime)
å
=
cba
m
f
)
7
,
5
,
3
,
2
,
1
(
Edges connecting two minterms corresponds to product that includes both minterms (the OR of the two adjacent minterms).
Text: Dally §6.4
(apply “combining” rule)
Notes: Specifically, we focus on the edge highlighted in blue here that connects cba=010 with cba=011.
What is a single product term that is true only when the input is either cba=010 or cba=011?
The answer is B. Notice only input a changes, if we replace input a with an X we obtain 01X. We can directly transform this into a product term by complementing inputs corresponding to a 0 and leaving out inputs with an X. This results in the Boolean expression NOT c AND b. Notice that since cba=010 is an implicant and cba=011 is an implicant, the expression is true if the input cba is either 010 or 011 and so it is also an implicant. Also note that 010 is binary for 2 and 011 is binary for 3. Both are prime numbers.
To summarize, the edge connecting two minterms corresponds to a single product term that includes both minterms.
This single product term it is the result of OR-ing together the Boolean expression for the two adjacent minterms, then applying the combining rule.
Now let us consider four adjacent implicants highlighted here. We can apply the same approach one by one to each of the four edges connecting these four vertices. This would result in four product terms each with two variables. However, we can do better.

## Slide 24: Cube representation (3-bit prime)
å
=
cba
m
f
)
7
,
5
,
3
,
2
,
1
(
Two edges that differ in one variable (e.g., 1X1 and 0X1) are said to be “adjacent”.
The face that includes both edges represents product that includes vertices for both edges.
Text: Dally §6.4
(apply “combining” rule)
Notes: Consider the edge represented by the product term 1X1 and the parallel edge here represented by the product term 0X1. Notice that these two edges differ only in the value of the first variable. In the top edge the first variable is 1 and in the bottom it is 0.
We say such edges are “adjacent”.
Notice that the face of the cube highlighted in blue includes both edges. That means it includes all four vertices making up the end points of both edges.
Now the question arises: Can we combine the product terms representing the two edges into a single product term?
If we replace the value of the single input that changes between the two edges with an X we can represent all four vertices associated with the two edges using XX1.
Recall first input is c and the last input is a. So a Boolean expression representing the first edge is “c AND a” and a Boolean expression representing the second edge is “not c AND a”.
We can apply the combining rule to simplify this expression to just “a”. The expression consisting of just “a” turns out to be an implicant. It is true when inputs cba are equal to 001, 011, 101, and 111 which are binary for 1, 3, 5 and 7, which are inputs for which our 3-bit prime number function is specified to output the logic value 1.

## Slide 25: Cube representation (3-bit prime)
å
=
cba
m
f
)
7
,
5
,
3
,
2
,
1
(
Much fewer gates (and wires)
Text: Dally §6.4
Optimized function is sum over “largest” implicants that “cover” all implicant vertices
Notes: To obtain a single Boolean expression we must combine the implicant “NOT c AND b” representing the edge connecting implicants 010 and 011 with the implicant “a” from the prior slide.
We do this by OR-ing them together. The final optimized function is a sum over the “largest” implicants that “cover” all implicant vertices.
Compare this with the original unoptimized Boolean expression for the 3-bit prime number function. These two expressions compute exactly the same thing. However, the optimized one requires far fewer transistors to implement.

## Slide 26: 4-D Hypercube (4-bit prime)
In 4D also have eight volumes that represent products with three X’s.
E.g. 1XXX is outside (blue) cube
Text: Dally §6.4
Notes: Let us return now to consider the 4-input prime number function. This slide illustrates a 4-dimensional hypercube with the implicants of the 4-input prime number function highlighted. We require an additional dimension because we increased the number of inputs from 3 to 4. In addition to a 1D edge and a 2D face in the 4D hypercube we can have three X’s that represent a three dimensional volume.

## Slide 27: 4-bit Prime Number Function (cont)
f = (a d) V (b c d) V (a b c) V (a b c)
V
V
V
V
V
V
V
¯
¯
¯
¯
¯
Text: Dally §6.4
Notes: For the 4-input prime function we can optimize the logic implementation by using one 2D implicant representing a surface where all four vertices are implicants and three 1D implicants representing edges combining two implicants, as highlighted on the left.
These correspond to four product terms listed in the table on the right.
From this table we can directly write out the following sum-of-products Boolean expression at the bottom.
The cube representation can be extended to any number of inputs. However, as you can see, it becomes harder for us to visualize as the number of inputs increase. This is because it is hard to draw a hypercube in two dimensions. One key thing to take away from this discussion is that the combining rule can be used to group adjacent implicants resulting in optimized Boolean expressions that consume less hardware.
Next we will discuss the Karnaugh Map approach to optimizing Boolean expressions. The Karnaugh Map is simply a way to represent the above cube representations in a two dimensional table in such a way that adjacent vertices in the cube representation are adjacent cells in the table.

## Slide 28: Karnaugh Map
The Karnaugh Map (also called KMAP) is a table used to represent the same information as a cube but in an easier to inspect way.
We can easily optimize Boolean functions with 2-inputs, 3-inputs, and 4-inputs using KMAPs.
Beyond this it gets difficult.
At the end of this slide set we will briefly talk about an alternative approach that can be implemented by a computer for any number of inputs.
Notes: The Karnaugh Map (also called KMAP) is a table used to represent the same information as a cube but in an easier to inspect way.
We can easily optimize Boolean functions with 2-inputs, 3-inputs, and 4-inputs using KMAPs.
However, beyond 4-inputs it gets more difficult.
At the end of this slide set we will briefly talk about an alternative approach that can be implemented by a computer for any number of inputs.

## Slide 29: Karnaugh Map
Draw table where each square represents an “input condition”. I.e., some combination of assignment of the input values to 1 and 0. Input condition is another term for minterm.
Each square in the table is equivalent to a vertex in the cube representation.
Organize the squares in the table so that adjacent vertices in the cube representation are adjacent in the table.
Notes: To use a KMAP we first draw a table where each square represents an “input condition”. An input condition is some combination of assignments of the input variables to 1 and 0. The term “input condition” is essentially just another name for what we have been calling a “minterm”.
In the KMAP each square in the table is equivalent to a vertex in the cube representation.
The clever thing that Maurice Karnaugh, the inventor of the KMAP, discovered back around 1952 was a way to organize the squares in the table so that adjacent vertices in the cube representation are adjacent in the table.

## Slide 30: Consider 2-input function
Assume inputs are called A and B (can use anything).
22 = 4 combinations of input values 0 and 1. E.g., A=0 and B=0.
Need four squares to represent each input condition:
A
B
0
1
1
0
E.g., this square represents the input condition AB=11 (i.e., A=1 and B=1)
Arrange squares so input conditions that differ by one bit are adjacent. E.g., AB=00 adjacent to AB=10.
Notes: Let’s start by considering a Boolean function with two inputs.
---
We will call the inputs A and B though they can be named anything.
---
With two inputs there are 2^2 = 4 combinations of input values or input conditions. For example one input condition is A=0 and B=0.
---
If each square represents a different input condition, we need four squares to represent all four input conditions.
We will arrange these squares so that input conditions that differ by only one bit are adjacent. In this figure the top left square is for the input condition A=0 and B=0. The top right square is for the input condition A=0 and B=1. The bottom left square is for the input condition A=1 and B=0.
Finally, the bottom right square is for the input condition A=1 and B=1.
Notice we have arranged the squares so input conditions that differ by one bit are adjacent. For example AB=00 is adjacent to AB=10.

## Slide 31
Let’s cut the table in half and rotate the bottom half up
A
B
0
1
1
0
AB
01
00
AB
01
00
AB
01
00
11
10
11
10
11
10
AB
01
00
11
10
AB
01
00
11
10
AB
01
00
11
10
Adjacent squares still represent input conditions that differ by one bit assuming we include wrap around.

## Slide 32
Wrap around as if squares inscribed on a cylinder as pictured below:

## Slide 33: Table for 3-input function
As with 2-input case, want adjacent squares to represent input conditions that differ only in one bit position. Must include wrap around.
A
0
1
BC
01
00
11
10
Notes: Now let us consider a table for a 3-input function. As with the 2-input case, we want adjacent squares to represent input conditions that differ only in one bit position.
What is the input condition that corresponds to the highlighted square in the KMAP?
The answer is 110. We read the value of A off of the vertical axis labels and the value of B and C off of the horizontal axis labels.
Note that the input condition ABC=000 is adjacent to ABC=010 if we include the wrap around edges. These two input conditions differ only in the value of B.

## Slide 34: KMAP for 4-input function
Need to include wrap around for both horizontal and vertical directions.
01
00
11
10
00
01
11
10
CD
AB
Notes: We can also draw a table for a 4-input function. Note for the 4-input case we need to include wrap around edges for both horizontal and vertical directions.

## Slide 35: Simplified Labels
Brackets indicate rows or columns for which designated input is 1 while zero otherwise.
C
A
B
D
Notes: We can make the task of drawing a KMAP easier by simplifying it as shown here. The rows or columns within a bracket are those in which the designated input has the value 1, while it is 0 elsewhere.

## Slide 36: Adding Implicants
Place a ‘1’ inside squares for which the output of the function is a ‘1’ (i.e., implicants).
Can put a ‘0’ in remaining squares (or leave empty and imagine there is a ‘0’ there)
Notes: So far we have only talked about the inputs of the function. To use the KMAP table we need to add the implicants inside the squares that correspond to their input conditions.
We will place a ‘1’ inside squares for which the output of the function is a ‘1’ -- i.e., for the implicant minterms.
Can also put a ‘0’ in the remaining squares although to save time you can simply leave them empty and imagine there is a ‘0’ in these squares.
Let us now return to our example of the 4-input prime number function and compare how our 4D hypercube is related to the four input KMAP.

## Slide 37: Karnaugh Map (K-Map) of 4-bit Prime
0
1
1
1
0
1
1
0
0
1
3
2
4
5
7
6
8
9
1
1
1
0
1
2
1
3
1
5
1
4
0
0
0
1
1
1
1
0
a
b
c
d
0
1
0
0
0
0
1
0
00
01
11
10
dc
ba
a
b
c
d
Text: Dally §6.5
Notes: Here is the 4-input prime number function with implicants highlighted on a 4D hypercube.
The four dimensions a, b, c and d are illustrated in the lower left.
On the right is a corresponding KMAP. We have added a 1 inside the squares for input conditions that correspond to implicants. We have added a 0 in the remaining squares.
The numbers in light grey inside each square illustrate the input value in decimal. They are added here for illustration only. Let us consider the input condition dcba=1101 which is binary for 13. As this is a prime number it is an implicant of the desired function.
Here, on the left, we have highlighted the vertex on the hypercube that corresponds to this input condition. On the right we have highlighted the corresponding square in the KMAP table that represents this input condition.
Next let us consider an adjacent implicant in the 4D hypercube such as dcba=0101.
Which square in the KMAP corresponds to the vertex labeled 0101 in the hypercube?
The answer is 5. Notice that the corresponding square is adjacent to the prior square.
This was not by accident. Any two vertices that are adjacent in the hypercube will be adjacent in the KMAP provided we include wrap around edges.
Let’s look at another example. On the left I have highlighted the vertex corresponding to the input being equal to 3. On the right I have highlighted the corresponding square in the KMAP.
Consider this adjacent vertex in the hypercube corresponding to the input being equal to 11 in decimal, which is 1011 in binary. On the KMAP the corresponding square is at the bottom of the map. Perhaps at first this does not seem adjacent to the other square.
However, remember we need to include wrap around edges in the KMAP.

## Slide 38: Karnaugh Map (K-Map) of 4-bit Prime
0
1
1
1
0
1
1
0
0
1
3
2
4
5
7
6
8
9
1
1
1
0
1
2
1
3
1
5
1
4
0
0
0
1
1
1
1
0
a
b
c
d
0
1
0
0
0
0
1
0
00
01
11
10
dc
ba
a
b
c
d
Text: Dally §6.5
Notes: Finally, consider the implicant containing the four vertices highlighted here on the left. The corresponding squares are adjacent in the KMAP. Next we are going to consider how to perform the same combining we performed using the cube representation but using the KMAP.
Before we move on, I would like to address a question that often arises when using the KMAP. The question is “does it matter where the input variables go on the sides of the KMAP?” For example, what if instead of having “dc” on the vertical direction and “ba” on the horizontal direction in our KMAP we used “ab” on the vertical and “cd” on the horizontal? Such changes do not matter in any fundamental way, as both KMAPs will be equivalent representations of the same underlying hypercube representation.

## Slide 39
Position of minterms on a 4-bit Karnaugh map
NOTE: we don’t normally draw the minterm
numbers inside a K-Map – we do it here for
explanation purposes only
0
1
3
2
4
5
7
6
ba
a
12
13
15
14
8
9
11
10
00
01
11
10
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Minterms
Text: Dally §6.5
Notes: To see how the KMAP can be used to optimize logic I am going to fill in each square in the KMAP with the value of the input condition (i.e., minterm number). The input conditions that are implicants are highlighted in blue. As noted earlier we normally put the single bit output value, not the input condition, inside the squares in a K-Map – we are using the input condition here instead so we can see more clearly how and why the KMAP actually works.

## Slide 40
0000
00
01
11
10
0001
0011
0010
0100
0101
0111
0110
1100
1101
1111
1110
1000
1001
1011
1010
Adjacent minterms differ in exactly one bit
Every blue minterm is an implicant
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Implicants
Text: Dally §6.5
Notes: Let’s re-write the input conditions in binary.
Now, let’s consider two adjacent squares.
Notice that the input value differs in only a single bit position between these two squares.
Now consider the product term that corresponds to the first implicant. As in earlier examples, each input variable that is zero for this input condition is complemented in the product term. Let’s compare this expression with the corresponding one for the adjacent input condition.
The product terms differ in only one position. Hence, we can apply the combining rule to simplify the logic implementation.
We can cover both input conditions with a single product term of three variables.
Let’s consider another two adjacent squares.
The input value in these two squares only differs in a single bit position.

## Slide 41
0000
00
01
11
10
0001
001X
0100
X101
0111
0110
1100
1111
1110
1000
1001
1011
1010
Can combine adjacent minterms into “larger” implicants
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Larger Implicants
Text: Dally §6.5
Notes: As with the cube representation, we can combine inputs for adjacent squares in the KMAP. Here we combine 0011 and 0010 into a single implicant 001X. Similarly we combine 0101 and 1101 into a single implicant X101.

## Slide 42
0000
00
01
11
10
0001
0011
0010
0100
0101
0111
0110
1100
1101
1111
1110
1000
1001
1011
1010
Remember wrap around edges -- both vertical as shown here and horizontal.
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Implicants
Text: Dally §6.5
Notes: We need to also consider wrap around edges when looking for implicants to combine. That goes for both vertical as illustrated here as well as horizontal.

## Slide 43
0000
00
01
11
10
0001
0010
0100
X101
0111
0110
1100
1111
1110
1000
1001
X011
1010
X011
Can combine adjacent minterms into implicants
Note edges wrap around
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Adjacency
Text: Dally §6.5
Notes: Here we combine 0011 and 1011 into X011.

## Slide 44
0000
00
01
11
10
0001
0011
0010
0100
0101
0111
0110
1100
1101
1111
1110
1000
1001
1011
1010
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: Implicants
Text: Dally §6.5
Notes: Let’s consider four squares that are adjacent. Notice each differs from it’s neighbor by one bit position.
We can combine all four implicant input conditions 0001, 0011, 0101, and 0111 into a single implicant 0XX1.

## Slide 45
0000
00
01
11
10
0XX1
0010
0100
0110
1100
1101
1111
1110
1000
1001
1011
1010
A larger implicant
ba
a
00
01
11
10
d
b
c
dc
Karnaugh Map of 4-bit Prime: 0XX1
Text: Dally §6.5
Notes: We call an implicant that covers more minterms a larger implicant.

## Slide 46: Optimization with a KMAP
Combine adjacent implicant minterms by circling largest rectangle with power of two sides (equivalent to product term). Want product term for each implicant.
Notes: To optimize a Boolean function with a KMAP we fill in the appropriate size KMAP table with a 1 for each implicant. Then, we combine adjacent implicant minterms by circling the largest rectangle with power of two sides. This restriction is important. A rectangle with power of two sides in the KMAP corresponds with an edge, surface or volume in the cube representation.
We want to circle each implicant.
In the KMAP shown here, what is the largest implicant? More specifically, the largest group of 1’s corresponding to a single product term includes which minterms?
The answer is C. The minterms 1, 3, 5 and 7 are adjacent in the KMAP and can be combined into a single product term. We can do this with a square that has sides of length 2 which is a power of 2.
Can we group the minterms 3 and 2?
The answer is yes. We can group them because they are adjacent and doing so corresponds to a rectangle with power of two sides. The width is 2 and the height is 1.
Can we group the minterms 1, 15 and 13 i.e., represent all three with a single product term?
The answer is no. While we could draw a rectangle around the three of them it would have height of three, which is not a power of two. Note that in the cube representation these three minterms would be on only 3 out of 4 vertices of a surface of the cube.
Can we group 3 and 11?
The answer is yes. These two squares are adjacent if one considers wrap around edges.

## Slide 47: Selecting a Cover
Select a minimum cost “cover”
A set of implicants is a cover of a
function if each minterm of the
function is included in at least
one implicant of the cover.
Cost of implicant is number of
variables in product.
Notes: Once we have circled enough largest implicants such that every implicant minterm is included in at least one circle, we need to select a minimum cost cover.
A set of implicants is a cover of a function if each minterm of the function is included in at least one implicant of the cover.
The cost of an implicant can be taken to be the number of variables in its product representation. Generally, that is smaller the larger the rectangle used to group the implicants. We will talk later about a strategy to select a minimum cost cover.

## Slide 48: Writing out product terms
Any input that a circle includes both with value 1 and 0 is eliminated from the product term.
C
A
B
D
1
1
1
1
f = A  C
Notes: Once we have found an optimized cover, we can write out the equation corresponding to the optimized Boolean logic.
We do this by determining the product term that corresponds to each circled group of implicants.
For each circled group of implicants we can directly write out the optimized product term by including only inputs for which the input value is constant. If a constant input is zero then the variable appears complemented in the product term.
We can quickly identify which inputs are eliminated by examining whether the circle is in two rows or two columns for which that input has different values. For example, here we have circled four minterms. The circle is in a row for which the input B is 1 and a row for which the input B is 0. Hence, B should not appear in the product term. We can also see that some of the minterms are in a column for which input D is 1 and some are in a column for which input D is 0. Hence, D should not appear in the final product term for this implicant. The final product term contains A and C. The A is complemented because it is zero for the rows in which the output is one.

## Slide 49: Writing Optimized Equation
Determine product term corresponding to each circled group of implicants
00
01
11
10
a
c
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
001X
X101
00
01
11
10
X011
0
X
X
1
dcba
b
vs.
Terminology: Prime implicant is an implicant
which cannot be made larger.
Notes: Let’s apply this procedure to our KMAP for the 4-input prime number function.
What is the product term corresponding the circled group of edges?
The answer is D.
To see why, let’s consider each input variable in turn.
The circled implicant minterms are in rows for which input d is zero. Hence D should appear complemented in the product term.
On the other hand, there are ones both in rows for which the input C is zero and others for which it is one. Hence C should not be included.
Similarly, the circled implicants are in columns for which input B is zero and one. Hence, B should not be included.
Finally, the circled implicants are only in columns for which the input A is one. Hence A should appear uncomplemented in the product term.
What is the product term corresponding to the red circled group of ones?
The answer is A.
To see why, we can follow the same procedure as before. The circled implicants are only in a row for which the inputs D and C are zero so D and C should appear complemented in the optimized product term. The circled implicants span the two columns where B is one so B appears uncomplemented. Finally, some of the implicants are in a column where A is 1 while others are in a column where A is 0 so we do not include A in the optimized product.
The reason we choose the red rectangle was that we need to cover the implicant dcba = 0010. Now, given we had already circled the implicant dcba = 0011 with the blue rectangle, you might be wondering why we would want to include it in the red rectangle. I.e., you might think that since it is already covered we should not try to cover it again. However, if instead we only circled dcba = 0010 instead of a product term with three variables d, c, and b, we would require a product term with all four input variables. So, we selected the red circle because it is the largest implicant that contains dcba = 0010.
Such an implicant, which cannot be made larger is called a prime implicant. Please note that the terminology “prime implicant” is unrelated to “prime” as used in the 4-bit prime number function we have been using throughout this lecture. That is, all Boolean functions have prime implicants.
Later we will see that another reason to select an implicant that overlaps is to eliminate something called a hazard.
Let’s continue generating the optimized expressions.
What is the product term corresponding to the magenta circled group of ones?
The answer is B.
What is the product term corresponding to the green circled group of ones?
The answer is B.

## Slide 50: Essential Prime Implicants
If a prime implicant, x, of a function f is the only prime implicant that contains a particular minterm y of the function f, we say that x is an essential prime implicant; x is essential because no other prime implicant includes y.
In prior example, all prime implicants are essential prime implicants. E.g., 0010 only contained in 001X so 001X is essential.
Text: Dally §6.4
Notes: 2.5

## Slide 51: Select “Inexpensive” Cover
Start with an empty cover;
Add all essential prime implicants to the cover;
For each remaining uncovered minterm, add the largest implicant that covers that minterm to the cover.
Text: Dally §6.6
Notes: Next let us return to the question of how to select a minimum cost cover.
Step 1 is to start with an empty cover;
Step 2 is to add all essential prime implicants to the cover;
Step 3 is, for each remaining uncovered minterm, add the largest implicant that covers that minterm to the cover.

## Slide 52
00
01
11
10
a
b
d
0
0
0
0
0
0
1
1
1
1
1
1
0
0
1
0
ba
dc
001X
X101
0XX1
00
01
11
10
X011
As we have seen, CMOS gates are
always inverting, so the real circuit
might look like this
Text: Dally §6.6, §6.7
f = (a d) V (b c d) V (a b c) V (a b c)
V
V
V
V
V
V
V
¯
¯
¯
¯
¯
Notes: Let’s put everything together. Given a specification of a Boolean function, for example a truth table or English language description, we draw a KMAP table with size dictated by the number of input variables. Then we label where the input variables go using a grey code which means only one bit changes at a time going from one row or column to the next. We then take the implicant minterms and place a 1 in their corresponding square of the KMAP. We then find a cover for the implicants by circling each essential prime implicant. In the 4-bit prime number example we have been discussing this results in all implicant input conditions being covered as shown here.
Next, we determine the product term that corresponds to each circled group of implicants. We do that by writing the variable complemented if the input is a constant zero for all circled implicants. We write the variable uncomplemented if that input is a constant one for all circled implicants. If the input variable takes on both 0 and 1, then we do not include it in the product term.
You might find it easier to first write out the input values in a table like that shown on the left before writing out the product terms as a Boolean expression as shown below. Note that the resulting Boolean expression is in a sum of product form.
Finally, you should be able to take the optimized Boolean equation or even just the list of implicants in the cover such as the one on the left and draw out a corresponding logic diagram as shown here on the right.
Let’s discuss one interesting real world detail here. Recall from prior lectures that CMOS gates are always inverting. Using AND and OR gates are expensive as they include an inverter. If we use NAND circuits we can reduce the total number of transistors in the circuit if we instead draw it like shown below on the right. You should be able to transform the circuit above into the one below. This is easy to do if you recall that two inverters back to back cancel each other out. Also, the OR gate with all complemented inputs is logically equivalent to a four input NAND gate. To see this recall deMorgan’s law.

## Slide 53: Two- and Three-Variable K-Maps
Two variable K-Map
(minterm positions)
Used same way as Four variable K-Map.
Three variable K-Map
(minterm positions)
Text: Dally §6.5
Notes: In the 4-bit prime number function example we had four input variables and so needed a KMAP with 2 to the power 4 equals 16 squares. For a 2-input function we saw previously we need four squares in our KMAP and for a 3-input function we saw earlier we need eight squares. This slide shows these KMAPS again. You use them just like the larger KMAP. Again, it is important to remember wrap around edges.

## Slide 54: Incompletely Specified Functions
Often we know certain input combinations will never occur. For these inputs, we do not care what the output of the function is.
We can exploit this “don’t care” input-output information to further optimize the circuit.
For example, suppose only need to detect 4-bit prime numbers less than 10 (decimal primes)…
Text: Dally §6.8
Notes: Often we know certain input combinations will never occur. For these inputs, we do not care what the output of the function is.
We can exploit this “don’t care” input-output information to further optimize the circuit.
For example, suppose only need to detect 4-bit prime numbers that are less than 10. We’ll call these decimal primes.

## Slide 55: Decimal prime number function – includes don’t cares
00
01
11
10
00
01
11
10
a
b
c
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
Text: Dally §6.8
Notes: This slide shows our KMAP for the 4-bit prime number function with one change. For all input conditions for which the input value is ten or greater, we have filled in the corresponding square an X. This X indicated we do not care whether the output for this input condition is a 1 or a 0. We will see we can use these X’s to increase the size of our implicants thus reducing the size of the eventual circuit.
We can also represent the don’t cares in our Boolean shorthand with a capital D followed by a list of minter numbers that correspond to these squares.

## Slide 56
Decimal prime number function K-Map
11
10
01
11
a
b
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
X1X1
00
01
11
10
X01X
0XX1
XX11
c
Text: Dally §6.8
Notes: Now we can include or not include X’s inside our implicants.
For example, the implicant X1X1 can be included as it includes either 1’s or X’s but no 0’s.
What is the Boolean expression for X1X1?
The answer is B. After circling an implicant including don’t cares, we follow the exact same procedure as before to identify the corresponding product term.
Now, here is another implicant that overlaps the first one.
If 0XX1 is already in cover does including X1X1 in cover also reduce hardware cost to implement the decimal prime function?
The answer is no. Since the only 1’s covered by X1X1 are already covered by 0XX1 there is no advantage to including X1X1.
Now, does the red circled group of minterms correspond to a single product term?
The answer is no. Since the height of the rectangle is 3 which is not a power of 2, we cannot this group of minterms does not correspond to a single product term.
Is there any other way to combine four minterms?
The answer is yes. This might be surprising. Remember we have to consider wrap around edges. This results in allowing us to add the implicant X01X.
Notice we have also added the implicant XX11. Clearly there are many more product term implicants than necessary to cover every minterm implicant.
Which implicants result in the minimum cost cover?
The answer is D. If we include the two implicants X01X and 0XX1 into our cover this results in the minimum cost.

## Slide 57
Cover:
0XX1
X01X
f = (a d) V (b c)
V
V
¯
¯
Decimal prime number function – circuit
00
01
11
10
a
b
d
0
0
x
0
0
0
1
1
1
1
1
x
x
x
x
x
ba
dc
00
01
11
10
X01X
0XX1
c
Text: Dally §6.6, 6.8
Notes: Now let’s consider how the use of don’t cares impacts the cost of the resulting circuit. Here we show the resulting cover we just identified.
You should by this point know how to transform this cover into the following Boolean equation. If you don’t review the earlier parts of this lecture.
You should also know how to transform this set of Boolean equations into the following logic gate diagram. Let’s compare this with the optimized function for the full 4-bit prime number function where we did not use any don’t cares.

## Slide 58
Impact of Using Don’t Cares
Optimized 4-bit Prime number function
Optimized 4-bit Decimal Prime number
function (specified with don’t cares)
Notes: On the left is the optimized circuit for the 4-bit prime number function. We can see it uses four 3-input NAND gates, three inverters and one 4-input NAND gate at the output. If you refer back to the lecture on CMOS gates from Slide Set 2 you can readily compute that this circuit will require 38 transistors.
Compare this to the optimized circuit for the 3-bit prime number function on the right. It uses three two input NAND gates and two inverters. This requires only 16 transistors. Thus the impact on the circuit would be a reduction in area of about 58%. This is obviously a big savings!

## Slide 59: Product-of-Sums Implementation
Sum-of-Products circuit: focus on inputs states where truth table is a 1.
Product-of-Sums: focus on input states where truth table is a 0.
1
1
1
1
1
1
1
1
0
1
3
2
4
5
7
6
8
9
11
10
12
13
15
14
00
01
11
10
ba
dc
1
0
1
1
0
1
0
0
a
b
c
d
1
0
0
1
1
1
1
1
d
c
a
Ú
Ú
Text: Dally §6.9
Notes: So far we have been discussing optimization in terms of circuits that represent a Boolean function in a sum of products form. As a consequence of the principle of duality for Boolean logic, we can also consider the dual form, which is the product of sums. We can also apply our KMAP approach to optimizing a circuit represented as a product of sums.
A product of sums equation can be represented using the shorthand shown here on the left. The capital M stands for “maxterm”. “A maxterm is a sum (i.e., logical OR) that includes every variable or its complement. Each 0 in a truth table or K-map corresponds to a maxterm.” The logic function in the KMAP at the bottom includes maxterms 0 and 2. For example, the maxterm 0 corresponds to a sum including all inputs with their value complemented, as shown in the first sum on the right.
To optimize a Sum-of-Products circuit we focus on inputs states where truth table is a 1.
To optimize a Product-of-Sums circuit we focus on input states where truth table is a 0.
For example, to optimize the circuit with the logic function implied by this KMAP for a product of sums implementation, we circle the largest power of two length side rectangles containing all 0’s or don’t cares. These largest circled groups of 0’s are called prime sums instead of prime implicants. In this case there is only one prime sum.
To write down the corresponding Boolean expression to a prime sum, we again consider whether the inputs are a constant value for all maxterms that are circled. If an input is a constant 1, then it appears complemented in the sum. If an input is a constant 0, then it appears uncomplemented in the sum.
You might be wondering whether this product of sums business is all nice theory and has no real world value. The reason I bring it up is that for any given circuit the smallest circuit may be either a sum of products form or a product of sums form. That said, when implemented in CMOS the sum of products form is typically a bit faster for reasons you’ll learn about in fourth year if you take ELEC 403.

## Slide 60: Product-of-Sums Example: Decimal Prime
0
1
1
1
0
1
1
0
0
1
3
2
4
5
7
6
8
9
11
10
12
13
15
14
00
01
11
10
ba
dc
1
0
1
1
0
1
0
0
a
b
c
d
x
x
x
x
0
0
x
x
d
c
a
Ú
b
a
Ú
Text: Dally §6.9
Notes: Let’s reconsider our decimal prime number example and look at the result of optimizing for a product of sums implementation. The results are shown below. If we drew out the logic gate diagram using NOR gates and inverters it would require two 2-input NOR gates, two inverters and a single 3-input NOR gate. This in turn would require 18 transistors which is more than the 16 required for the sum of products form.

## Slide 61: Hazards
0
0
1
1
0
1
1
0
0
1
3
2
4
5
7
6
0
0
0
1
1
1
1
0
b
a
c
1
0
a
b
c
Static-1 hazard
c
b
c
a
v
v
Text: Dally §6.10
1
1ns
2ns
3ns
4ns
5ns
6ns
0ns
Time:
1
1
0
0
1
1
0
@Time=1ns
0 @ Time=2ns
0
1
@ Time=4ns
1
@ Time=5ns
1





@ Time = 3ns
 @ 6ns
Notes: 3

## Slide 62: Cover transitions to eliminate hazards
0
0
1
1
0
1
1
0
0
1
3
2
4
5
7
6
0
0
0
1
1
1
1
0
b
a
c
1
0
a
b
c
c
b
c
a
b
a
v
v
v
Text: Dally §6.10
Notes: When we find a cover during our KMAP optimization we can include additional implicants to ensure any two adjacent squares are covered by the same implicant. An example is shown here. Notice we have added the implicant a AND b. This makes our circuit slightly larger, but it will consume less energy. As an aside, this is an example of a common them in engineering which is that there are often tradeoffs between different design objectives.

## Slide 63: Quine-McCluskey Algorithm
1. Start with implicant minterms in rightmost column.
2. Replace a bit with X and test whether result is an implicant;
if succeed add to next column. Repeat.
Number of variables |  |  | 
4 | 3 | 2 | 1
0001 |  |  | 
0010 |  |  | 
0011 |  |  | 
0101 |  |  | 
0111 |  |  | 
1011 |  |  | 
1101 |  |  | 
Text: Dally §6.4
Is 000X an implicant?
0000
0001
Fails test
Step 2.1
Step 2.2
00X1 ?
0001 ✔
0011 ✔
Passes test
If cannot replace any bit with X, then implicant is a prime implicant. Cannot be made larger. (Note: This use of “prime” unrelated to “prime number” function).
Number of variables |  |  | 
4 | 3 | 2 | 1
0001 | 00X1 |  | 
0010 |  |  | 
0011 |  |  | 
0101 |  |  | 
0111 |  |  | 
1011 |  |  | 
1101 |  |  | 
Number of variables |  |  | 
4 | 3 | 2 | 1
0001 | 00X1 | 0XX1 | 
0010 | 0X01 |  | 
0011 | 001X |  | 
0101 | 0X11 |  | 
0111 | X011 |  | 
1011 | 01X1 |  | 
1101 | X101 |  | 
Number of variables |  |  | 
4 | 3 | 2 | 1
0001 | 00X1 | 0XX1 | 
0010 | 0X01 |  | 
0011 | 001X |  | 
0101 | 0X11 |  | 
0111 | X011 |  | 
1011 | 01X1 |  | 
1101 | X101 |  | 
0000 ✖ (not implicant)
0001 ✔
Notes: Finally, you might be wondering how a tool like Quartus can optimize logic functions. For example, does it use a KMAP? The KMAP was introduced back in 1952 as a visual aid to help a designer manually constructing circuits. However, even back then it was recognized as primarily an important aid to helping develop understanding and intuition. In 1956 a fully automated approach was proposed by McCluskey. It is now called the Quine-McCluskey algorithm and as it is fairly straightforward, we’ll describe how it works.
As you can see the algorithm uses a table. Each column heading indicates the number of variables present in an implicant representing a product term that is listed under it.
To start, we fill in the first column, which is for implicants with four input variables, with the implicants from the abbreviated truth table representation of the function. In the above table we have the implicant minterms of the 4-bit prime number function.
Next we repeatedly replace a bit from one of the implicants with an X and test whether the result is an implicant.
If it is an implicant, it will have one less input variable and we can enter it into the next column. We then repeat this process until we find no more new implicants.
For example, lets consider the first implicant minterm circled here.
We apply step 2 the first time.
We will start with the rightmost bit.
Replacing this bit with X results in 000X. Is 000X an implicant?
Recall that the X represents both 0 and 1. So 000X really represents both the minterm 0000 and 0001.
Now, while 0001 is an implicant 0000 is NOT an implicant. Hence 000X is NOT an implicant.
So, it fails the test.
Let’s repeat Step 2.
This time we will try the second bit from the right.
Is 00X1 an implicant?
It is! The reason is that 00X1 represents the two minterms 0001 and 0011 and all of these are implicants themselves.
Hence, 00X1 passes the test.
Thus, we add 00X1 to the next column.
Continuing like this we would fill out the entire table like so. One thing to note is this is a very time consuming process. You would not want to actually apply the Quine-McCluskly algorithm manually. However, repeating such simple steps is perfectly suited to a computer.
Note that while applying Step 2 we may find we cannot any bit in a given implicant with an X and pass the test. Such cases correspond to essential prime implicants, which we defined earlier.
Here I have highlighted in blue, the essential prime implicants. You may recognize some of them from our earlier example of optimizing the 4-bit prime number function with a KMAP. This is not by accident. The essential prime implicants are unique and do not depend upon which algorithm we use to find them.
You may be wondering if you need to know how to apply the Quine-McCluskey algorithm on a test. Don’t worry because you don’t. The important point to remember about this slide is that tools like Quartus will optimize your logic much like we do with a KMAP. This has implications for how you should spend your time when designing a circuit using Verilog. In particular, it means when using Verilog you should not spend any time trying to optimize the logic yourself.