## Slide 1: CPEN 211: Computer Systems I Slide Set 4: Combinational Logic Building Blocks (1)
Instructor: Tor Aamodt
[Image: Roman Geometric Mosaic. There are some hardware combinational logic designs we use repeatedly, not unlike patterns found in art and nature
Source Wikipedia, By Mbellaccini - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=38150120]
Notes: 1

## Slide 2: Learning Objectives
After this slide set you should be able to:
Explain what a one-hot code is
Explain the operation of the following combinational building blocks and use them in your own hardware designs :
  Decoder (binary to one-hot)
  Encoder (one-hot to binary)
  Multiplexer (select one of N)
Notes: 2

## Slide 3: Combinational Building Blocks
Text: Dally §8
There are some combinational circuits that appear very frequently. Makes sense to design these “once” and then reuse them.
Learning these is also a great way to practice translating from a logic diagram to Verilog and vis versa.
Notes: 0.5

## Slide 4
[image source: https://www.partsnotincluded.com/researching-time-circuit-led-displays/]

## Slide 5: Example: Seven-Segment Decoder
?
0000 (“0”)
0001 (“1”)
0010 (“2”)
…
0111111
0000110
1011011
…

## Slide 6: One-hot representation
Represent a set of N elements with N bits
Exactly one bit is set to 1 (all other bits are 0)
Example – encode numbers 0-7:
Binary One-hot
000 00000001
001 00000010
010 00000100
… …
110 01000000
111 10000000
Text: Dally §8.2
Notes: 3

## Slide 7
Suppose we are given a number in binary and want to build a circuit that converts this to the corresponding one-hot code.
How might you design such a circuit?
Write out the truth table then, for each output bit draw a KMAP.
However, this is such a common circuit, it has a name…

## Slide 8: Decoder
A decoder converts symbols from one code to another.
A binary to one-hot decoder converts a symbol from binary code to a one-hot code.
Used to construct memory (return to see how later)
Binary input a to one-hot output b
b[i] = 1 if a = i
(or b = 1<<a)
n
m
a
n
m
2
≤
b
Decoder
Text: Dally §8.2
Notes: 3

## Slide 9: Example of a Decoder
2 4 Decoder
a1 | a0 | b3 | b2 | b1 | b0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Text: Dally §8.2
a1 | a0 | b0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a1 | a0 | b1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Notes: 2

## Slide 10: Example of a Decoder
2 4 Decoder
a1 | a0 | b3 | b2 | b1 | b0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
1
1
0
0
0
0
0
1
1
0
1
1
0
0
0
1
Text: Dally §8.2
Notes: 2

## Slide 11: 3:8 decoder
a2 | a1 | a0 | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
⁞ |  |  | ⁞ |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 12: Encoder
An encoder is an inverse of a decoder.
Encoder is a logic module that converts a one-hot input signal to a binary-encoded output signal.
Example: a 4 2 encoder.
a3 | a2 | a1 | a0 | b1 | b0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
b0 = a3  a1
b1 = a3  a2
Text: Dally §8.4
Notes: 3

## Slide 13: How to choose one of two different inputs in a digital circuit?

## Slide 14: Multiplexer
Often want to select one thing out of many possibilities.
Example: Pick either A0 or A1 as input to module.
Solution: Use a combinational logic block with three inputs select, A0 and A1 where the value of select says whether the output is equal to A0 or A1.
So common, this circuit is given a name, “multiplexer” (or “mux” for short):
Text: Dally §8.3
0
1
Operation: If select is zero then b = A0 otherwise b = A1
0
1
Notes: 3.5

## Slide 15: Multiplexer Select Encoding
What is best encoding for “select”?
Two common encodings:
Binary: select=0 means b=A0,
select=1 means b=A1
One hot: select=01 means b=A0
select=10 means b=A1
Text: Dally §8.3
Notes: 3.5

## Slide 16: Example: k-bit, 4 to 1 multiplexer with one-hot select
If select = 0001, then b = a0
If select = 0010, then b = a1
If select = 0100, then b = a2
If select = 1000, then b = a3

## Slide 17: Multiplexer
Multiplexer:
  n k-bit inputs
  n-bit one-hot select signal s
  Multiplexers are commonly used as data selectors
Selects one of n k-bit inputs
s must be one-hot
b=a[i] if s [i] = 1
Text: Dally §8.3
Notes: 3.5

## Slide 18: Multiplexer (n=2,k=1)
s1 | s0 | A0 | A1 | b
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
0
1
1
1
1
Question: How to build this circuit out of gates?

## Slide 19: Let’s design this multiplexer…
s1 | s0 | A0 | A1 | b
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 

## Slide 20: Multiplexer Implementation
k=1, n=4
1
0
1
0
1
1
0
0
0
0
1
0
1
Text: Dally §8.3
Notes: 3

## Slide 21
1-bit, 2-input One-Hot Select Mux
Symbol:
Implementation with
AND and OR gates:

## Slide 22
2-bit, 3-input Mux

## Slide 23: k-bit Binary-Select Multiplexer
Selects one of n k-bit inputs
s must be one-hot
b=a[i] if s [i] = 1
Text: Dally §8.3
Start with one hot select mux:
Notes: 3

## Slide 24: 1-bit, 4-input: Binary-Select Multiplexer
k=1, m=2, n=4
3-input AND gates result from combining two 2-input AND gates: one from decoder and one from one-hot select Mux.
Text: Dally §8.3
Add decoder:
Notes: 1.5

## Slide 25: Recall: Tri-state inverter
e=0, a=1
e | a | x
0 | 0 | Z
0 | 1 | Z
1 | 0 | 1
1 | 1 | 0

## Slide 26: Multiplexer Implementation
k=1, n=4
1
0
1
0
1
1
0
0
0
0
1
0
1
Tri-State Buffer
Text: Dally §8.3
Notes: 3

## Slide 27: Recall: Shannon Expansion
Can factor any Boolean function of n-inputs:
For prime function (F=1 if is prime or 1):
E.g., Expand around
1
1
i
s
p
r
i
m
e
0
1

## Slide 28
Next, expand around :
0
1
x2
1
2
i
s
p
r
i
m
e
x1
x0
0
1
2
3

## Slide 29
3
i
s
p
r
i
m
e
0
1
1
1
0
1
0
1
Logic with Muxes
Muxb
Text: Dally §8.3
0
1
x2
1
2
i
s
p
r
i
m
e
x1
x0
0
1
2
3
x1
x0
x2

## Slide 30: What’s Inside an FPGA?

## Slide 31: What’s Inside an FPGA?
Basic Logic Gate: Lookup-Table
Function of each lookup table can be configured by shifting in bit-stream. Lookup table is basically a hardware implementation of a “truth table” storing the output for each different input in one of the rows.
Inputs
Muxb
Bit-Stream (.sof file)
3
0
1
1
1
0
1
0
1
Truth table for isprime:

## Slide 32: FPGA Logic Block:
Mux selects between output of lookup table, or flip-flop
that connects to output of lookup table. Mux select input is programmed by configuration bit-stream as well.
Inputs
Muxb
3
Lookup Table

## Slide 33: What’s Inside an FPGA?

## Slide 34: Reconfigurable Logic:
Connect Logic Blocks using Fixed Metal Tracks and Programmable Switches

## Slide 35: Memory
Notes: This figure shows an abstracted view of main memory in a computer. The main memory is on the right and is connected to the processor on the left…
… using a bus…

## Slide 36: Memory
Memory is one of the most important structures inside a computer (or any digital system)
Memory is composed of large number of locations that can be uniquely identified and can store a value
“8 gigabytes (8GB)” means 8 billion memory locations*, each containing 1 byte (8-bits) of information.
Each location is uniquely identified by its “address”
Total number of locations is called the “address space”
Number of bits stored in each location is “addressability”
Let’s look at a special type of memory called read-only memory (ROM) – values cannot be modified
* Actually, 8 x 1024 x 1024 x 1024 = 8,589,934,592 locations

## Slide 37: Read-only memory (ROM)
Text: Dally §8.8
Above ROM contains 2n (read-only) memory locations each storing m-bits of data
Notes: 2

## Slide 38: Example Read Only Memory (n=2, m=1)
Stored Data:
22 x 1-bit words
Switch
Simplified view (e.g., omits logic for controlling switches)
This memory stores 22 = 4 “words” where each word is 1-bit
Each address is 2-bits long.
Address space contains 4 locations.
Addressability is 1-bit.

## Slide 39: Example: n=2, m=1
“0” on “control input”
means switch “open”
“1” on “control input”
means switch “open”

## Slide 40
Read-only memory (ROM) – internal structure
Text: Dally §8.8
“Tri-state driver” – acts
Like a switch where input
on side of triangle is “control input”.
Notes: 2

## Slide 41
2-D array implementation
Text: Dally §8.8
Notes: 3

## Slide 42: What’s Inside an FPGA? Continued…
FPGA vendors embed fixed blocks to improve speed and density:
Embedded Memories (blocks of 2K-18K)
To use these memory blocks we
Need to follow the coding
Style in the Quartus manual

## Slide 43: What’s Inside an FPGA?
FPGA vendors embed fixed blocks to improve speed and density:
Embedded Memories (blocks of 2K-18K)
Multiplier Blocks

## Slide 44: What’s Inside an FPGA?
FPGA vendors embed fixed blocks to improve speed and density:
Embedded Memories (blocks of 2K-18K)
Multiplier Blocks
High-Speed I/Os
Dedicated Clock Circuitry
CPU (eg. ARM Cortex-A9
in Cyclone V on DE1-SoC)

## Slide 45: Factoring
Many combinational blocks can be built up out of multiple smaller versions of the same block

## Slide 46: Example: 4-Input Binary Select Multiplexer
Text: Dally §8.3

## Slide 47: Example: 4-Input Binary Select Multiplexer
Text: Dally §8.3

## Slide 48: Designing A Large Encoder – 164 from five 42s
a
[
1
5
:
1
2
]
4
a
[
1
1
:
8
]
4
a
[
7
:
4
]
4
a
[
3
:
0
]
4
2
2
2
2
b
[
1
:
0
]
b
[
3
:
2
]
2
2
First, encode lower 2 bits.
Next, want to encode upper 2 bits. Can do that with an encoder where input is one hot vector summarizing which encoder has a one on input.
4:2
4:2
4:2
4:2
4:2
One hot
input
Text: Dally §8.4
0000
0000
0010
0000
00
01
00
00
0
0
1
0
01
01
0
0
0
1
3 2 1 0
7 6 5 4
11 10 9 8
15 14 13 12
High bits
Low bits
Notes: 3

## Slide 49: Example: Larger Decoders
Decoders used for constructing memory are LARGE (e.g., 6:64, 7:128, etc…)
Building large decoder using same approach as for 2:4 and 3:8 is inefficient
Want to build a large decoder using fewer transistors

## Slide 50
Don’t freak out if you don’t understand the next ~15 slides. You will do fine in this course even if you don’t get this example.
It is however a useful and “interesting” example

## Slide 51: Reconsider 2:4 Decoder
yb
y1
y0
yb | y1 | y0
0 | 0 | 1
1 | 1 | 0
Truth Table
A 1:2 decoder!
Text: Dally §8.2

## Slide 52: Reconsider 2:4 Decoder
yb
y1
y0
xb
x1
x0
2:4 decoder can be built out of two 1:2 decoders combined using four AND gates.
One AND gate for each output.
How to extend to larger decoders?
Hard part: Knowing which small decoder outputs to AND together.
Text: Dally §8.2

## Slide 53: Geometric Interpretation: Big picture
Divide input bus into N smaller busses such that every input wire is part of just one of the smaller buses
Any input bus value has a corresponding set of values assigned to each of the N smaller busses.
Let the smaller busses specify positions in an N-dimensional space. Notice: Each point in this space corresponds to just one input value.
Let each decoder output be represented by one of these positions.
Use AND gate to verify each of the N smaller busses has the value that corresponds to this output.
Simplify AND gate inputs by using one-hot code.

## Slide 54: 2:4 Decoder Geometric Interpretation
(xb,yb) specify coordinate in Euclidean space:
The 2:4 decoder output that has value of 1 indicates which point (xb,yb) corresponds to.
xb
yb
0
1
1
0
Text: Dally §8.2

## Slide 55: 2:4 Decoder Geometric Interpretation
(xb,yb) specify coordinate in Euclidean space:
The 2:4 decoder output that has value of 1 indicates which point (xb,yb) corresponds to.
xb
yb
0
1
1
0
a
b
Decoder
{xb,yb}=002
1
0
0
0
Text: Dally §8.2

## Slide 56: 2:4 Decoder Geometric Interpretation
(xb,yb) specify coordinate in Euclidean space:
The 2:4 decoder output that has value of 1 indicates which point (xb,yb) corresponds to.
xb
yb
0
1
1
0
a
b
Decoder
0
1
0
0
{xb,yb}=012
Text: Dally §8.2

## Slide 57: 2:4 Decoder Geometric Interpretation
(xb,yb) specify coordinate in Euclidean space:
The 2:4 decoder output that has value of 1 indicates which point (xb,yb) corresponds to.
xb
yb
0
1
1
0
a
b
Decoder
0
0
1
0
{xb,yb}=102
Text: Dally §8.2

## Slide 58: 2:4 Decoder Geometric Interpretation
(xb,yb) specify coordinate in Euclidean space:
The 2:4 decoder output that has value of 1 indicates which point (xb,yb) corresponds to.
xb
yb
0
1
1
0
a
b
Decoder
0
0
0
1
{xb,yb}=112
Text: Dally §8.2

## Slide 59: 2:4 Decoder Geometric Interpretation
(x1,x0) is one-hot code indicating x value
(y1,y0) is one-hot code indicating y value
x0=1
x1=1
y1=1
y0=1
xb
yb
Text: Dally §8.2

## Slide 60: 2:4 Decoder Geometric Interpretation
(x1,x0) is one-hot code indicating x-dimension
(y1,y0) is one-hot code indicating y-dimension
b[0] is 1 when x0 = 1 AND y0 = 1
Same as “b0 = x0 ⋀ y0”
a
b
Decoder
1
0
0
0
xb
yb
x0=1
y0=1
Text: Dally §8.2
{xb,yb}=002
002
010

## Slide 61: 2:4 Decoder Geometric Interpretation
(x1,x0) is one-hot code indicating x-dimension
(y1,y0) is one-hot code indicating y-dimension
b[1] is 1 when x0 = 1 AND y1 = 1
Same as “b1 = x0 ⋀ y1;”
a
b
Decoder
0
1
0
0
xb
yb
x0=1
y1=1
Text: Dally §8.2
{xb,yb}=012
012
110

## Slide 62: 2:4 Decoder Geometric Interpretation
(x1,x0) is one-hot code indicating x-dimension
(y1,y0) is one-hot code indicating y-dimension
b[2] is 1 when x1 = 1 AND y0 = 1
Same as “b2 = x1 ⋀ y0;”
a
b
Decoder
0
0
1
0
xb
yb
x1=1
y0=1
Text: Dally §8.2
{xb,yb}=102
102
210

## Slide 63: 2:4 Decoder Geometric Interpretation
(x1,x0) is one-hot code indicating x-dimension
(y1,y0) is one-hot code indicating y-dimension
b[3] is 1 when x1 = 1 AND y1 = 1
Same as “b3 = x1 ⋀ y1;”
a
b
Decoder
0
0
0
1
xb
yb
x1=1
y1=1
Text: Dally §8.2
{xb,yb}=112
112
310

## Slide 64: 6:64 Decoder Geometric Interpretation
Build 6  64 decoder from three 2  4 decoders
  Think of each bit of output as one point in a cube
Each 24 decodes 2 bits of input “a”
  a[5:4]x[3:0]
  a[3:2]y[3:0]
  a[1:0]z[3:0]
a1 | a0 | z3 | z2 | z1 | z0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
a3 | a2 | y3 | y2 | y1 | y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
a5 | a4 | x3 | x2 | x1 | x0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Example: input a = 011010
Text: Dally §8.2
Notes: 3

## Slide 65: 2-Stage decoder
Text: Dally §8.2
Notes: 2

## Slide 66: Advantage Of Dividing Large Decoder
6->64 decoder requires:
  64 6-input AND gates (384 inputs)
6->64 decoder using 2->4 decoders requires:
  12 2-input AND gates (24 inputs)
  64 3-input AND gates (192 inputs)
Faster, smaller, lower power
Text: Dally §8.2
Notes: 1.5

## Slide 67: Summary
We learned about three combinational logic building blocks: decoder, encoder, mux
We saw how to design them using truth tables and optimize them using Boolean algebra
Learned how an FPGA works
Saw how a read-only-memory works.
Saw how to build larger building blocks out of smaller building blocks.