## Slide 1: CPEN 211: Introduction to Microcomputers Slide Set 8: Iterative Combinational Logic
Prof. Tor Aamodt
[ Background image: Logic gate diagram for a portion of the PDP 11 data path; The PDP 11 was a famous “minicomputer” from the 1970s.
Copyright © DEC. Source: http://www.psych.usyd.edu.au/pdp-11/Images/11_20_dp.gif ]
Notes: 0.5

## Slide 2: Learning Objectives
By the end of this slide set you should be able to:
Design an iterative combinational logic circuit
Describe iterative combinational logic in Verilog
Notes: 2

## Slide 3: Hexadecimal numbers
Hexadecimal, ‘hex’, or base-16, number system is very convenient when working with computers.
Mainly, it is shorter and faster to write than binary.
It is far easier to convert between binary and ‘hex’ than between binary and decimal.
Four bits can represent 24 = 16 different things.
We take four bits, give them the 16 labels 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F

## Slide 4: Hexadecimal numbers
Binary | Decimal | Hexadecimal
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | 8
1001 | 9 | 9
1010 | 10 | A
1011 | 11 | B
1100 | 12 | C
1101 | 13 | D
1110 | 14 | E
1111 | 15 | F

## Slide 5: From Decimal To Binary To Hexadecimal
Example: 196310
196310 = 0111 1010 10112
Ahex
Bhex
7
Text: Dally §10.1
Notes: 1963-1024=939
939-512=427
427-256=171
171-128=43
43-32=11
11-8=3
3-2=1
1-1=0

## Slide 6: Example: Arbiter
Arbiter handles requests from multiple devices to use a single resource.
E.g.: Single resource is road inside intersection
Text: Dally §8.5
[https://en.wikipedia.org/wiki/All-way_stop#/media/File:4waystop.jpg]
Notes: 1.5

## Slide 7: Arbiter
Finds first “1” bit in input r
g[i]=1 iff r[i]==1 and, for j<i, r[j]==0
Another way of saying this: picks lowest input set to 1 as the single winner and grants this winner’s request.
NOTE: output is one-hot code (or all zero if no requests).
Arbiter handles requests from multiple devices to use a single resource. Responds to requests (r) with grants (g).
n
n
Arbiter
r
g
Text: Dally §8.5
Notes: 3.5

## Slide 8: How to build an Arbiter?

## Slide 9: Iterative Circuit Design (1/4)
Any combinational logic circuit can be implemented as sum-of-products. So, could design an arbiter that way.
However, some combinational logic circuits, called “iterative circuits” have outputs that follow a pattern.
Arbiter is such an example.
We can use our knowledge of the specific pattern to help design the circuit.

## Slide 10: Iterative Circuit Design (2/4)
In an iterative circuit the number of output bits depends upon number of input bits. E.g., for the arbiter r and g are both n bits.
In an iterative circuit the output in position “i” is a function of the input(s) at position “i” along with the inputs at all earlier positions.
What makes the circuit “iterative” is that we can find a way to summarize the inputs from earlier bit positions using a small number of bits (e.g., a single bit).

## Slide 11: Iterative Circuit Design (3/4)
The summary is often call a carry signal.
Each bit position has a carry-in (ci-1) and a carry-out (ci).
ci
ci+1
xi
yi

## Slide 12: Iterative Circuit Design (4/4)
We build the circuit by making many identical copies of the same circuit and connecting the carry-out of one stage to the carry-in of the next circuit. First bit position connect carry-in to a fixed value.
c0
c1
x0
y0
c2
x1
y1
cn-1
cn
xn-1
yn-1
…

## Slide 13: Iterative Circuit Design - Steps
Encode carry by identifying information in earlier bit positions relevant to current bit position. No recipe. Requires creativity.
Write truth table for output and carry-out at position i. The inputs in this truth table are the circuit’s input at bit position i and the carry-out generated from bit position i-1.
Write out the logic function for bit position i (perhaps using a KMAP to optimize it).
Make n copies of this circuit connecting carry-out of position i-1 to carry-in of position i.

## Slide 14
For arbiter: g[i]=1 iff r[i]==1 and, for j<i, r[j]==0
Notes: First step, finding this equation from “Finds first 1 bit in input r”. Could write out a few examples and see the equation holds.
Could write out truth table for each output bit, that would work. Would take a long time.
Instead, will recognize there is a pattern to the logic (e.g., equation). Try to build iterative circuit.
Notice condition divides into two part separated by AND.
Second part suggests need a new signal, call it ”t” and t[i] means for j<i, r[j]==0

## Slide 15: Logic Diagram Of One Bit Of An Arbiter
Text: Dally §8.5
Notes: 2

## Slide 16: Implementation of a 4-Bit Arbiter
Using Bit-Cell
1
0
1
0
1
1
0
0
0
0
1
0
0
Text: Dally §8.5
g[i]=1 iff r[i]==1 and, for j<i, r[j]==0
Notes: 2

## Slide 17: Implementing Arbiter Using Verilog
// arbiter stage
module ArbStage(r, cin, g, cout) ;
input r, cin ;
output g, cout ;
assign cout = ~r & cin ;
assign g = r & cin ;
endmodule
cin
cout

## Slide 18: Implementing Arbiter Using Verilog
// arbiter – version #1: hierarchical
module Arb(r, g) ;
input [3:0] r ;
output [3:0] g ;
wire [4:0] c ;
assign c[0] = 1’b1;
ArbStage stage1(r[0], c[0], g[0], c[1]);
ArbStage stage2(r[1], c[1], g[1], c[2]);
ArbStage stage3(r[2], c[2], g[2], c[3]);
ArbStage stage4(r[3], c[3], g[3], c[4]);
endmodule
1

## Slide 19: Implementing Arbiter – Version #2
// arbiter – version #2: gate level
module Arb(r, g) ;
input [3:0] r ;
output [3:0] g ;
wire [3:0] c ;
assign c[0] = 1'b1;
assign c[1] = ~r[0] & c[0];
assign c[2] = ~r[1] & c[1];
assign c[3] = ~r[2] & c[2];
assign g = r & c;
endmodule
1
c0
c1
c2
c3
Notes: Use this example to introduce alternative and commonly used bit-slice notation:
assign c = {~r[2] & c[2], ~r[1] & c[1], ~r[0] & c[0], 1’b1 };
assign c = {~r[2:0] & c[2:0], 1’b1 };

## Slide 20: Implementing Arbiter – Version #3
// arbiter – version #3: bit-slice
module Arb(r, g) ;
input [3:0] r ;
output [3:0] g ;
wire [3:0] c ;
//assign c[0] = 1'b1;
//assign c[1] = ~r[0] & c[0];
//assign c[2] = ~r[1] & c[1];
//assign c[3] = ~r[2] & c[2];
assign c = {(~r[2:0] & c[2:0]),1'b1};
assign g = r & c;
endmodule
1
“iterative” combinational logic circuit using bit-slice style:
We use {a, b} for concatenation
We use r[2:0] and c[2:0] for index ranges

## Slide 21: Example: Implementing Arbitrary Width Arbiter Using Verilog
// arbiter (arbitrary width)
module Arb(r, g) ;
parameter n=4 ;
input [n-1:0] r ;
output [n-1:0] g ;
wire [n-1:0] c ;
wire [n-1:0] g ;
assign c = {(~r[n-2:0] & c[n-2:0]),1'b1} ;
assign g = r & c ;
endmodule
Text: Dally §8.5
Highlighted line is equivalent to:
assign c[0] = 1'b1;
assign c[1] = ~r[0] & c[0];
assign c[2] = ~r[1] & c[1];
…
assign c[n-1] = ~r[n-2] & c[n-2];
Notes: 3

## Slide 22: Priority Encoder
Priority Encoder:
  n-bit input signal a
  m-bit output signal b
    b indicates, in binary, the position of the first 1 bit in a (starting from least significant bit)
m
n
m = log2n
a
b
Priority
Encoder
1010
01
Text: Dally §8.5
n
n
m
r
g
Arbiter
ae
b
Encoder
a
b
0010
Notes: 3.5

## Slide 23: Verilog for Priority Encoder
// priority encoder (arbitrary width)
module PriorityEncoder83(r, b) ;
input [7:0] r ;
output [2:0] b ;
wire [7:0] g ;
Arb #(8) a(r, g) ;
Enc83 e(g, b) ;
endmodule
Text: Dally §8.5
Notes: 1.5

## Slide 24: Functions built from decoders and other blocks
Example – find maximum of 256 small 4-bit numbers
  Decode each number 416 bits (256 times)
  OR these together w/16 256-bit ORs
    (each a 4-level tree of 4-input ORs)
  Use an Arbiter to get highest of 16
  Encode the 164
Need to see if this is more efficient than a tournament
Can this determine which input has the ‘winning’ number?
Decode
OR
Arbiter
Encode
Text: Dally §8.2 + 8.5
Notes: 3

## Slide 25: Comparing Values
Comparing two 1-bit signals for equality:
a | b | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XNOR gate
Text: Dally §8.6
Notes: 1.5

## Slide 26: Equality Comparator
// equality comparator
module EqComp(a, b, eq) ;
parameter k=8;
input [k-1:0] a,b;
output eq;
wire eq;
assign eq = (a==b) ;
endmodule
a=b
Comparing two n-bit signals for equality:
Text: Dally §8.6
Notes: 2.5

## Slide 27: Magnitude Comparator
a > b
A > B iff A[i] > B[i] and A[k] = B[k] for k > i.
A = 0 1 1 0 0 1 1 0 1 0
B = 0 1 0 1 0 1 0 1 0 0
AgtB =
0
1
0
1
1
1
0
1
1
1
Text: Dally §8.6
Notes: 2.5

## Slide 28
A > B iff A[i] > B[i] and A[k] = B[k] for k > i.
Text: Dally §8.6
Notes: 2.5

## Slide 29: Magnitude Comparator
// magnitude comparator
module MagComp(a, b, gt) ;
parameter k=8 ;
input [k-1:0] a, b ;
output gt ;
wire [k-1:0] eqi = a ~^ b ;
wire [k-1:0] gti = a & ~b ;
wire [k:0] gtb = {((eqi[k-1:0] & gtb[k-1:0]) | gti[k-1:0]), 1’b0} ;
wire gt = gtb[k] ;
endmodule
A > B iff A[i] > B[i] and A[j] = B[j] for j > i.
Text: Dally §8.6
Equivalent to writing:
assign gtb[0] = 1'b0;
assign gtb[1] = (eqi[0] & gtb[0]) | gti[0];
assign gtb[2] = (eqi[1] & gtb[1]) | gti[1];
…
Notes: 2.5

## Slide 30: Another Implementation Of Magnitude Comparator
Text: Dally §8.6
Notes: 2

## Slide 31
// Behavioral Magnitude comparator
module MagComp_b(a, b, gt) ;
parameter k=8 ;
input [k-1:0] a, b ;
output gt ;
wire gt = (a > b) ;
endmodule
Text: Dally §8.6
Notes: 1.5

## Slide 32: Putting things together – Maximum unit
a
n
b
b
n
a
n
m
a
x
n
n
a > b
1
0
gt
Magnitude
Comparator
Mux
Text: Dally §9.3
Notes: 2

## Slide 33: Summary
Learned about iterative combinational logic