## Slide 1: CPEN 211: Introduction to Microcomputers Slide Set 10: Adder Circuits, Two’s Complement
Prof. Tor Aamodt
[ Background image: Logic gate diagram for a portion of the PDP 11 data path; The PDP 11 was a famous “minicomputer” from the 1970s.
Copyright © DEC. Source: http://www.psych.usyd.edu.au/pdp-11/Images/11_20_dp.gif ]
Notes: 0.5

## Slide 2: Learning Objectives
By the end of this slide set you should be able to:
Explain how addition is performed using combinational logic
Represent negative numbers in 2’s complement
Build an efficient adder/subtractor unit
Notes: 2

## Slide 3: Addition
We can design an iterative combinational logic circuit to perform addition…
Inputs:
  A = (an-1,an-2,…,a1,a0)
  B = (bn-1,bn-2,…,b1,b0)
Output:
  Sum = (sn-1,sn-2,…,s1,s0)
Carry?

## Slide 4
Binary addition
1-bit 0+0 = 0, 1+0 = 1, 1+1 = 10
1
  6 110 + 3 011
  5 101 +7 111
0_
10_
01
001
110_
1001
9
0
1_
00
11_
100
111_
1100
12
Text: Dally §10.2
carry-in
carry-out

## Slide 5: One bit of an adder
Counts the number of “1” bits on its input
Outputs the result in binary
For a half-adder, 2 inputs, output can be 0, 1, or 2
For a full-adder, 3 inputs, output can be 0, 1, 2, or 3
Text: Dally §10.2

## Slide 6: Half Adder
// half adder
module HalfAdder(a,b,c,s);
input a,b ;
output c,s ; // carry and sum
wire s = a ^ b ;
wire c = a & b ;
endmodule
ab cs
# 00 00
# 01 01
# 10 01
# 11 10
Text: Dally §10.2

## Slide 7
Full Adder
Counts the number of “1” bits on its input
For a full-adder, 3 inputs, output can be 0, 1, 2, or 3
Full adder symbol:
Text: Dally §10.2

## Slide 8: Full adder from a truth table
Text: Dally §10.2

## Slide 9: Full adder from truth table
// full adder - logical
module FullAdder2(a,b,cin,cout,s) ;
input a,b,cin ;
output cout,s ; // carry and sum
wire s = a ^ b ^ cin ;
wire cout = (a & b)|(a & cin)|(b & cin) ; // majority
endmodule
Text: Dally §10.2

## Slide 10
Full Adder via Factoring
Can build (smaller) full-adder out of half adders…
Text: Dally §10.2
half adder
ab cs
# 00 00
# 01 01
# 10 01
# 11 10

## Slide 11
// full adder - from half adders
module FullAdder1(a,b,cin,cout,s) ;
input a,b,cin ;
output cout,s ; // carry and sum
wire g,p ; // generate and propagate
wire cp ;
HalfAdder ha1(a,b,g,p) ;
HalfAdder ha2(cin,p,cp,s) ;
assign cout = g | cp;
endmodule
# 000 00
# 001 01
# 010 01
# 011 10
# 100 01
# 101 10
# 110 10
# 111 11
Text: Dally §10.2

## Slide 12: Adder in Verilog - behavioral
// multi-bit adder - behavioral
module Adder1(a,b,cin,cout,s) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input cin ;
output [n-1:0] s ;
output cout ;
wire [n-1:0] s;
wire cout ;
assign {cout, s} = a + b + cin ;
endmodule
Text: Dally §10.2
Verilog automatically zero extends “cin” to be n bits for this addition.

## Slide 13: Multi-bit Adder
Text: Dally §10.2
1
  6 110 + 3 011
0_
10_
01
001
110_
1001
9

## Slide 14
p
g
c[i]
c[i+1]
a[i]
b[i]
s[i]
p[i]: Propagate carry in position i if a[i] or b[i] is 1
g[i]: Generate carry in position i if both a[i] and b[i] are 1

## Slide 15: Ripple-carry adder – bit-slice notation
// multi-bit adder – with vectors
module Adder2(a,b,cin,cout,s) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input cin ;
output [n-1:0] s ;
output cout ;
wire [n-1:0] p = a ^ b ;
wire [n-1:0] g = a & b ;
wire [n:0] c = {g | (p & c[n-1:0]), cin} ;
wire [n-1:0] s = p ^ c[n-1:0] ;
wire cout = c[n] ;
endmodule
Text: Dally §10.2

## Slide 16: Negative Integers
Thus far we have only addressed positive integers. What about negative numbers?
3 ways to represent negative integers in binary:
  Sign Magnitude
  One’s complement
  Two’s complement
Example: Consider +23 –23
  Sign Magnitude 0 10111 1 10111
  One’s complement 0 10111 1 01000
  Two’s complement 0 10111 1 01001
Text: Dally §10.3

## Slide 17: Converting Positive to Negative
To convert a positive number in 2’s complement to a negative number:
invert bits and then add 1
E.g., convert 0011 to negative number:
step 1: 1100 (flip all bits)
step 2: 1100+0001 (add one)
1101 (-3 in 2’s complement)
Text: Dally §10.3

## Slide 18: Converting Negative to Positive
Use same operation to convert back
E.g., convert 1101 (-3) to positive number:
step 1: 0010 (flip all bits)
step 2: 0010+0001 (add one)
0011 (3 in 2’s complement)
Text: Dally §10.3

## Slide 19: Why do we use 2’s complement?
2’s complement makes subtraction easy
Represent negative number, –x as 2n – x
All arithmetic is done modulo 2n so no adjustments are necessary
x + (– y) = (x + (2n – y)) mod 2n
consider 4-bit numbers
4 – 3 = 4 + (– 3)
= (4 + (16 – 3)) mod 16 // 4+(16-3) = 17; 17 mod 16 = 1 = 4 + (15 – 3 + 1)
= 4 + (15 – 3) + 1 = 0100 + (1111 – 0011) + 0001
= 0100 + (1100) + 0001 = 0001
Text: Dally §10.3

## Slide 20: 2’s Complement
Text: Dally §10.3
1 = 0001
-1 = 1110 + 1 = 1111
7 = 0111
-7 = 1000+1 = 1001
Interesting case: -8
5-bits:
8 = 01000
-8 = 10111 + 1 = 11000
Note: Lower 4-bit same!
Want MSB to indicate
negative number, so in 4-bits:
1000 is -8

## Slide 21
Text: Dally §10.3
Value Function (2’s Complement)
Assume bi is value of ith bit in 2’s complement representation of a number, then
Example, n=4:
-810 = 10002 = (-23 • 1) + (0 • 20) + (0 • 21) + (0 • 20)

## Slide 22: Impact of <signed> (s) in Verilog Bit Literals…
wire [7:0] a;
assign a = <val>;
<val>
2’b10 // a == 8’b0000_0010 (zero extended)
2’b01 // a == 8’b0000_0001
2’sb10 // a == 8’b1111_1110 (sign extended)
2’sb01 // a == 8’b0000_0001
Note: “Does not work” with “x” – use {n{x}} to get n x’s.

## Slide 23
Text: Dally §10.3
2’s Complement Adder/Subtractor

## Slide 24
Overflow
If using 4-bits, 4 + 4 = 8 which cannot fit into 4-bit (recall, 1000 means -8 if using 4-bit 2’s complement)
If using 4-bits, -6 + (-3) = -9 which doesn’t fit in 4-bits (lower 4-bits of 101112 is 01112 which is 710)
Observation: Inputs same sign, result different sign.
Text: Dally §10.3

## Slide 25
Detecting Overflow
Text: Dally §10.3
1 here if sign of A and B differ
1 here if sign of A and result differ
This works fine, but it turns out there is a more clever implementation that uses fewer gates...

## Slide 26
Alternative implementation
as | bs | cis | ss | cos | ovf | comment
0 | 0 | 0 | 0 | 0 | 0 | Both inputs positive, no overflow, carry in = carry out
0 | 0 | 1 | 1 | 0 | 1 | Both inputs positive, overflow, carry in != carry out
0 | 1 | 0 | 1 | 0 | 0 | Inputs signs different, no overflow, carry in = carry out
0 | 1 | 1 | 0 | 1 | 0 | Inputs signs different, no overflow, carry in = carry out
1 | 1 | 0 | 0 | 1 | 1 | Both inputs negative, overflow, carry in != carry out
1 | 1 | 1 | 1 | 1 | 0 | Both inputs negative, no overflow, carry in = carry out
Text: Dally §10.3
Let’s consider inputs and outputs of full-adder used to compute sign bit:
So we know there is an overflow if: carry in != carry out for the sign bit!

## Slide 27
Text: Dally §10.3

## Slide 28
// add a+b or subtract a-b, check for overflow
module AddSub(a,b,sub,s,ovf) ;
parameter n = 8 ;
input [n-1:0] a, b ;
input sub ; // subtract if sub=1, otherwise add
output [n-1:0] s ;
output ovf ; // 1 if overflow
wire c1, c2 ; // carry out of last two bits
wire ovf = c1 ^ c2 ; // overflow if signs don't match
// add non sign bits
Adder1 #(n-1) ai(a[n-2:0],b[n-2:0]^{n-1{sub}},sub,c1,s[n-2:0]) ;
// add sign bits
Adder1 #(1) as(a[n-1],b[n-1]^sub,c1,c2,s[n-1]) ;
endmodule
Text: Dally §10.3
// multi-bit adder – with vectors
module Adder2(a,b,cin,cout,s) ;

## Slide 29: Summary
Learned about addition and 2’s complement