## Slide 1: Slide Set 13: Timing

## Slide 2
⋮
⋮
Q: what are these numbers?
source: AMD

## Slide 3: Learning Objectives
By the end of this slide set you should be able to:
Define propagation delay, setup time, hold time, and clk-to-Q time
Explain how they arise from the transistor RC model
Finding the critical path given circuit (longest delay between flip-flops)
Perform timing analysis in Quartus
Explain how to fixing violations of setup time and hold time

## Slide 4: TL;DR: timing in a digital circuit
digital circuit = combinational logic in between flip-flop registers
gates have some propagation delay tprop
  ➔ how long it takes for gate output to stabilize after inputs change
slowest path between regs: critical path
  determines maximum clock frequency
combinational
logic
tprop
critical path

## Slide 5: Okay, but why is there a gate delay?
MOSFETs can be modelled as an RC circuit
  source/drain resistance Rs
  gate parasitic capacitance Cg
Rs
Rs
Cg
Cg
gate
source
drain
substrate
gate oxide

## Slide 6
time
voltage at gate

## Slide 7: Gate delays TL;DR
propagation delay across gates
delay longer if fanout is higher (b/c parallel capacitance adds)
connected gate delays accumulate
tprop
longer tprop
tprop1 + tprop2

## Slide 8: Timing analysis
I1
I2
A
B
I1 prop delay
I2 prop delay
Q: is this the
fastest clock?
problem: we didn’t account for flip-flop delays
(incomplete)

## Slide 9: Review: D flip-flops
D flip-flop = two latches in series
first captures input when clk is low
second takes over from the first when clk goes high
D
Q
clk
D
Q
D
Q
clk
G
G
what about timing? we need to look inside a latch

## Slide 10: Inside a latch: setup time and hold time
latches capture input in feedback loops
change only one input at a time, or else loop can go metastable*
to capture stable signal, D must be stable before and after G falls
these constraints are called setup time (tS) and hold time (tH)
D
Q
G
D
Q
G
Q
*details beyond the scope of 211, but it’s a bad thing™
Notes: setup time is because D changes have to propagate into the feedback loop
hold time is because G has to propagate to the feedback loop
actually the Earle latch and the SR latch need different analysis to figure out setup and hold times

## Slide 11: What about flip-flop propagation time?
DQ propagation time not well-defined — Q changes when clk rises
so actually we care about clock-to-Q time (tCQ)
D
clk
clk
Q
Notes: the analysis here depends on clk going from low to high

## Slide 12: D flip-flop timing constraints redux
tS: setup time — D input steady before posedge clk
  time to stabilize the first latch feedback loop before the gate (clock) changes
tH: hold time — D input steady after posedge clk
  time for the latch gate (clk) to propagate to isolate the first latch feedback loop
tCQ: clock-to-Q time — when output appears on Q after posedge clk
  time for the clock to propagate to the second latch output

## Slide 13: Flip-flop timing waveforms: setup and hold
setup time
hold time
clk
D
D
TL;DR: D input can’t change in the forbidden zone™
input arrives before clk – tS
input changes before clk + tH
input arrives too late
setup time violation
D
signal changes too early hold time violation

## Slide 14: Flip-flop timing waveforms: clock-to-Q
clk-to-Q propagation time
clk
output reflects DFF contents later,
at clk + tCQ
D
Q
DFF captures D input at rising clock edge*
*assuming the FF’s setup time and hold time are respected

## Slide 15: Timing constraints redux
propagation delay (gates)*
  how soon the output changes after an input change
setup time (flip-flops)
  how early before posedge clk the input has to become stable
hold time (flip-flops)
  how long after posedge clk the input must remain stable
clk-to-Q time (flip-flops)
  how soon after posedge clk the DFF’s contents appear on Q
*wires also have a tiny resistance and capacitance so also a tiny propagation delay, but we will ignore this in CPEN211

## Slide 16: Timing analysis: gate and flip-flop constraints
I1
I2
A
B
A’s
tCQ
I1 prop delay
I2 prop delay
B’s
tS
“slack”
minimum clk period =
tCQ
+ tprop,I1
+ tS
+ tprop,I2

## Slide 17: Timing analysis example
I1
I2
A
B
Q. min clk period [ns]?
I3
parameters: tS = 0.5ns tH = 0.6ns tCQ = 0.3ns tprop,INV = 1ns
Q. max frequency?
Q. slack at 100 MHz?
tCQ + 3×tprop,INV + tS = 0.3 + 3 + 0.5 = 3.8ns
1 / 3.8ns = 263.2 MHz
100MHz  10ns; 10 – 3.8 = 6.2ns
Q. met timing at 100MHz?
slack is positive  YES

## Slide 18: Fixing setup time violations
lower target clock frequency*
combinational logic optimization (e.g., replicate to reduce fanout)
pipelining (later lecture)
retiming (later lecture)
typically tools like Quartus do logic optimization and maybe retiming
*and hope for partial marks

## Slide 19: What about hold time?
suppose A’s input changes 0  1
A’s new output (1) will appear at clk + tCQ = clk + 0.3ns
no gate delays and ideal wires  output 1 gets to B at clk + 0.3ns
but B needed previous input (0) stable until clk + tH = clk + 0.6ns!
hold time violation
parameters: tS = 0.5ns tH = 0.6ns tCQ = 0.3ns tprop,INV = 1ns
A
B
*usually minimum clk-to-Q time < maximum clk-to-Q time; this example assumes they are equal

## Slide 20: Fixing hold time violations
problem: path too fast: A’s changes arrive at B’s inputs too early
  arrive at clk + tCQ = clk + 0.3ns, but needed to hold stable until clk + tH = 0.6ns
independent of clock frequency, so can’t fix with slower clock
how to make paths slower? add some gates on the path
  now arrive at clk + tCQ = clk + 0.3ns + 2ns = clk + 2.3ns ≥ clk + 0.6ns
parameters: tS = 0.5ns tH = 0.6ns tCQ = 0.3ns tprop,INV = 1ns
A
B

## Slide 21: Hold Violations Cont.
ts
th
signal changes too early hold time violation
clk
A
B
tCQ

## Slide 22: Hold Violations Cont.
ts
th
clk
A
B
tCQ
tprop

## Slide 23: Timing closure in practice
specify target frequency, I/O constraints, etc. in .sdc file
  create_clock -period 10 -name clk [get_ports clk]
  set_input_delay -clock clk 1 [all_inputs]
  set_output_delay -clock clk 1 [all_outputs]
Static Timing Analysis (STA) tools do the math we covered (+ more details)
  Quartus has one built-in
Quartus tries its best to meet timing
  logic optimization, retiming, buffers, …

## Slide 24
fastest clock Quartus could get
(not the 100MHz we wanted)
failed
analyzes fast/slow, hot/cold “corners”
– manufacturing variation
– external temp
– chip temp variations when running
critical path
delay
details

## Slide 25: Summary
what propagation delay, setup time, hold time, and clk-to-Q time are
how they arise from the transistor RC model
finding the critical path given circuit (longest delay between flip-flops)
timing analysis from constraints (max frequency, min period, slack, etc.)
ways of fixing violations of setup time and hold time