## Slide 1: CPEN 211: Introduction to Microcomputers Slide Set 12: Arbitrary Digital Systems
Prof. Tor Aamodt
[Background: Intel 45nm SRAM test chip;
Source: http://www.intel.com/pressroom/archive/releases/2006/20060125comp.htm]
Notes: 1

## Slide 2: Learning Objectives
By the end of this slide set you should be able to:
Implement any digital system by designing a FSM and corresponding datapath and writing Verilog.
Describe tri-state drivers in Verilog and understand how multiple drivers of a signal are handled in simulation

## Slide 3: Datapath/Control Partitioning
We can implement an arbitrary digital system by combining a control FSM and datapath
Text: Dally §16.3

## Slide 4
Partitioning into control FSM and datapath can be performed by high-level synthesis tools which employ various algorithms we are not going to cover in CPEN 211.
Best results are still usually obtained by a human designer manually partitioning a design. Do learn to do this we’ll walk through a couple of examples.

## Slide 5: Multiplier
Using a truth table it is possible to design a block that can multiply two numbers using only combinational logic:
Combinational Logic
A
B
Result = A*B

## Slide 6: Exponent
Now, suppose we want to build a circuit to calculate X3
Here X is an n-bit input, assume the result also fits in n bits for now

## Slide 7: Exponent: A bit more complicated
What if we want to compute XA where X and A are both inputs?
If A was fixed, we could figure out how many multipliers we need (as in the previous example).
But, during the operation of this circuit, suppose A can change.
How do we know how many hardware units to put down?

## Slide 8: Exponent: A bit more complicated
The algorithm to be implemented in this block:
P = 1; CNT = A-1;
while (CNT >= 0) do
P = P * X;
CNT = CNT – 1;
end while;
Note 1: this isn’t Verilog or C, it is just pseudo-code to illustrate the algorithm.
Note 2: We could write this in Verilog, but it would not be synthesizable. So, we have to design it using smaller blocks (each one synthesizable)

## Slide 9
Synthesis Rule that didn’t matter before: A synthesizable always block can only describe what happens in one clock cycle.
NOTE: If you have been following the style guidelines then you have implicitly been following this rule already.
The algorithm on the prior page would take more than one clock cycle. So, it would not be synthesizable.

## Slide 10
Consider this simple datapath:
If we let this run for A clock cycles, we will produce our result. This will work for any A.
P = 1; CNT = A-1;
while (CNT >= 0) do
P = P * X;
CNT = CNT – 1;
end while;

## Slide 11
Need a way to initialize P to 1 at the start:
First cycle, set selP and loadP to 1 and this will initialize P to 1
P = 1; CNT = A-1;
while (CNT >= 0) do
P = P * X;
CNT = CNT – 1;
end while;

## Slide 12
Need a way to initialize P to 1 at the start:
Next, set selP and loadP to 0; then P = P * X on next rising edge of clk.
We have to let this run for A cycles. We need some sort of counter to keep track of this.
P = 1; CNT = A-1;
while (CNT >= 0) do
P = P * X;
CNT = CNT – 1;
end while;

## Slide 13
Add a counter for CNT:
P = 1; CNT = A-1;
while (CNT >= 0) do
P = P * X;
CNT = CNT – 1;
end while;

## Slide 14
But we are not there yet. What we really want is:
So, to implement this, we need a controller that:
when s goes high:
set selP and selA to 1 for one cycle
wait until zero goes high
when it does, assert done, and go back to the start
reset

## Slide 15: How to design FSM Controller?
Manually, work out a timeline of what needs to happen on each rising edge of clock for sample inputs.
Use timeline to add states and determine outputs. Things to keep in mind while doing this:
  Each clock cycle corresponds to being in a given state in the FSM controller (might stay in a given state more than one cycle).
  The datapath update specified by the FSM control inputs occurs on the next rising edge (e.g., as you leave the state).

## Slide 16: Example Timeline: A=3, X=4
1st rising edge of clk: Reset FSM; Assume s=1, A=3, X=4
2nd rising edge of clk: Set P=1, CNT=A-1=2
  To do this need selP=1, loadP=1, selA=1 before rising edge
3rd rising edge of clk: s=1 => CNT=CNT-1=1, P = P * X = 4
  To do this need selP=0, loadP=1, selA=0 before rising edge
4th rising edge of clk: z=0,CNT=0, P = P * X = 16
5th rising edge of clk: z=1,CNT=-1, P = P * X = 64
6th rising edge of clk: leave P unchanged, set done = 1.
  To do this need selP=0, loadP=0, selA=0 before rising edge.

## Slide 17
Here is a simple controller that does that:
selP=1
loadP=1
selA=1
done=0
selP=0
loadP=1
selA=0
done=0
selP=0
loadP=0
selA=0
done=1
NOTE: In the rest of examples in this slide set we will not show outputs that are set to zero. If an output is not specified in a state, we assume it is zero and when writing Verilog you would still need make sure the output logic sets these signals to zero. They are not “don’t cares”!!!
reset

## Slide 18
Now combine the state machine and the datapath into one circuit:
selP
loadP
reset

## Slide 19
module top(clk,reset,X,A,s,P,done);
parameter n=8; // width of X and A
parameter m=8; // width of counter
input clk, reset;
input [n-1:0] X, A;
input s;
output [n-1:0] P;
output done;
// datapath for exponential circuit
datapath #(n,m) DATA( .clk(clk), .selP(selP),
.loadP(loadP), .selA(selA),
.A(A), .X(X), .P(P), .zero(zero) );
// FSM controller for exponential circuit
control CTRL( .clk(clk), .reset(reset), .s(s),
.zero(zero), .selP(selP), .loadP(loadP),
.selA(selA), .done(done) );
endmodule
Text: Dally §16.3

## Slide 20
wire [2*n-1:0] multiply_result = X * P; // n x n bit Multiplier
wire [n-1:0] multiply_init = selP ? 1 : multiply_result; // SelP Mux
wire [n-1:0] P_next = loadP ? multiply_init : P; // loadP multiplexer
vDFF #(n) ProductRegister(clk,P_next,P); // P hold current exponential
Text: Dally §16.3

## Slide 21
wire [m-1:0] count;
wire [m-1:0] count_init = selA ? A : count; // selA Multiplexer
wire [m-1:0] count_next = count_init - 1; // Subtract 1
vDFF #(m) CountRegister(clk,count_next,count); // counter state
wire zero = ~|count; // detects if count is zero
Text: Dally §16.3

## Slide 22
module datapath(clk,selP,loadP,selA,A,X,P,zero);
parameter n=8; // width of X and A
parameter m=8; // width of counter
input clk, selP, loadP, selA;
input [n-1:0] A, X;
output [n-1:0] P;
output zero;
// exponential computation
wire [2*n-1:0] multiply_result = X * P; // n x n bit Multiplier
wire [n-1:0] multiply_init = selP ? 1 : multiply_result; // SelP Mux
wire [n-1:0] P_next = loadP ? multiply_init : P; // loadP multiplexer
vDFF #(n) ProductRegister(clk,P_next,P); // P hold current exponential
// counter for sequencing computation
wire [m-1:0] count;
wire [m-1:0] count_init = selA ? A : count; // selA Multiplexer
wire [m-1:0] count_next = count_init - 1; // Subtract 1
vDFF #(m) CountRegister(clk,count_next,count); // counter state
wire zero = ~|count; // detects if count is zero
endmodule
Text: Dally §16.3

## Slide 23: Check Using Quartus RTL Viewer

## Slide 24
module control(clk,reset,s,zero,selP,loadP,selA,done);
input clk, reset, s, zero;
output selP, loadP, selA, done;
// state encoding for control FSM for exponent circuit
`define SW 2
`define Sa 2'b00
`define Sb 2'b01
`define Sc 2'b11
wire [`SW-1:0] present_state, state_next_reset, state_next;
reg [(`SW+4)-1:0] next;
// state DFF for control FSM for exponent circuit
vDFF #(`SW) STATE(clk,state_next_reset,present_state);
// reset mux for control FSM for exponent circuit
assign state_next_reset = reset ? `Sa : state_next;
// combinational logic for control FSM for exponent circuit
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: next = {`Sa, 4'b1110}; // Sa->Sa as long as s==0; SelP=loadP=selA=1
{`Sa,2'b1x}: next = {`Sb, 4'b1110}; // Sa->Sb when s==1; same outputs (Moore FSM)
{`Sb,2'bx0}: next = {`Sb, 4'b0100}; // Sb->Sb as long as zero==0; loadP=1
{`Sb,2'bx1}: next = {`Sc, 4'b0100}; // Sb->Sc once zero==1; same outputs (Moore FSM)
{`Sc,2'b0x}: next = {`Sc, 4'b0001}; // Sc->Sc as long as s==0; set done=1 to tell world we’re done
{`Sc,2'b1x}: next = {`Sa, 4'b0001}; // Sc->Sa once s==1 again (handshake with consumer of results)
default: next = {{`SW{1'bx}},{4{1'bx}}}; // only get here if present_state, s, or zero are x’s
endcase
// copy to module outputs
assign {state_next, selP, loadP, selA, done} = next;
endmodule
Text: Dally §16.3
selP=1
loadP=1
selA=1
done=0
selP=0
loadP=1
selA=0
done=0
selP=0
loadP=0
selA=0
done=1

## Slide 25
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: {state_next,selP,loadP,selA,done} = {`Sa,4'b1110};
Sa
Sb
Sc
match this case label if present_state == `Sa and….
selP=1
Text: Dally §16.3
loadP=1
loadP=1

## Slide 26
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: {state_next,selP,loadP,selA,done} = {`Sa,4'b1110};
Sa
Sb
Sc
… s == 0 and zero == 1 or 0
selP=1
Text: Dally §16.3
loadP=1
loadP=1

## Slide 27
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: {state_next,selP,loadP,selA,done} = {`Sa,4'b1110};
Sa
Sb
Sc
selP=1
Text: Dally §16.3
loadP=1
loadP=1
`Sa: if (s == 0) begin
state_next = `Sa;
{selP,loadP,selA,done} = 4’b1110;
end else begin ...

## Slide 28
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: {state_next,selP,loadP,selA,done} = {`Sa,4'b1110};
{`Sa,2'b1x}: {state_next,selP,loadP,selA,done} = {`Sb,4'b1110};
Both should be same for “Moore” state machine
If present_state == `Sa and s == 1 and zero == x
then
state_next = `Sb and
{selP,loadP,selA,done} = 4’b1110
Sc
selP=1
Text: Dally §16.3
loadP=1
loadP=1
Sa
Sb

## Slide 29
module control(clk,reset,s,zero,selP,loadP,selA,done);
input clk, reset, s, zero;
output selP, loadP, selA, done;
// state encoding for control FSM for exponent circuit
`define SW 2
`define Sa 2'b00
`define Sb 2'b01
`define Sc 2'b11
wire [`SW-1:0] present_state, state_next_reset, state_next;
reg [(`SW+4)-1:0] next;
// state DFF for control FSM for exponent circuit
vDFF #(`SW) STATE(clk,state_next_reset,present_state);
// reset mux for control FSM for exponent circuit
assign state_next_reset = reset ? `Sa : state_next;
// combinational logic for control FSM for exponent circuit
always @(*)
casex ( {present_state, s, zero} )
{`Sa,2'b0x}: next = {`Sa, 4'b1110}; // Sa->Sa as long as s==0; SelP=loadP=selA=1
{`Sa,2'b1x}: next = {`Sb, 4'b1110}; // Sa->Sb when s==1; same outputs (Moore FSM)
{`Sb,2'bx0}: next = {`Sb, 4'b0100}; // Sb->Sb as long as zero==0; loadP=1
{`Sb,2'bx1}: next = {`Sc, 4'b0100}; // Sb->Sc once zero==1; same outputs (Moore FSM)
{`Sc,2'b0x}: next = {`Sc, 4'b0001}; // Sc->Sc as long as s==0; set done=1 to tell world we’re done
{`Sc,2'b1x}: next = {`Sa, 4'b0001}; // Sc->Sa once s==1 again (handshake with consumer of results)
default: next = {{`SW{1'bx}},{4{1'bx}}}; // only get here if present_state, s, or zero are x’s
endcase
// copy to module outputs
assign {state_next, selP, loadP, selA, done} = next;
endmodule
Text: Dally §16.3
selP=1
loadP=1
selA=1
done=0
selP=0
loadP=1
selA=0
done=0
selP=0
loadP=0
selA=0
done=1

## Slide 30
module exponential_tb;
reg [7:0] A, X;
reg s, clk, reset;
wire [7:0] P;
wire done;
top DUT( .clk(clk), .reset(reset),
.X(X), .A(A), .s(s),. P(P),
.done(done) );
initial forever begin
clk = 0; #5;
clk = 1; #5;
end
initial begin
s = 1;
reset = 1;
A = 8'd3;
X = 8'd4;
#10
reset = 0;
#10
s = 0;
#40
$stop;
end
endmodule
[http://www.servicenoodle.com/lighthouse-auto-sales-and-repair-p-552966]
Text: Dally §16.3

## Slide 31: Reminder: Organizing your Waves

## Slide 32: Reminder: Adding internal signals

## Slide 33: Simulation results

## Slide 34: Tri-State Drivers
Tries to drive output node to 0 volts
Tries to drive output node to 3.3 volts
What voltage is this?

## Slide 35: Fighting
This is an example of “fighting”
- What happens depends on the
way the circuits are implemented
- For CMOS (most chips are
designed using CMOS), fighting
can cause high currents and
even damage the chip!
Interesting question: what would happen if we measure the voltage
of such a wire?

## Slide 36: Simulation
Now think of what happens if we simulate a Verilog specification of
this circuit…
What should the value of this output node be?
- We know a wire or reg can be ‘0’ or ‘1’
- But neither of those is the right answer.
- As we have seen, in simulation a possible values is ‘x’
- We have seen ‘x’ used for don’t care, but ‘x’ also means unknown
When ModelSim sees this fighting, it sets the value of the
output to ‘x’. That tells you something is wrong.
Remember, in the real circuit, the node will have some value… (can’t
measure an ‘x’ voltage using a multimeter)

## Slide 37: Recall: Tri-State Drivers
If “enable” is 1, then out is driven with the value on in.
If “enable” is 0, then out is not driven.
- What does that mean? If no one else is driving
this signal, then the signal is “floating”
- What happens if you try to measure the voltage of
a floating signal in the lab?
(We saw how to construct one of these with CMOS in Slide Set 2.)

## Slide 38: Simulation
Now think of what happens if we simulate a Verilog specification of
this circuit…
If enable is zero, what should the simulation say the output is?
- One of the possible values is ‘z’
- ‘z’ stands for high impedance
in enable out
0 0 z
1 0 z
0 1 0
1 1 1
Remember: in the real world, a signal will have a voltage, even if it is not being driven
- Can’t measure Z in the lab

## Slide 39
WRONG!
always @(*)
if (enable == 1'b1)
out = in;

## Slide 40
The problem with the previous specification is that if enable is zero,
the output is not driven. Verilog syntax says that in this case, the
output maintains its old value.
- Not the behaviour we want to specify

## Slide 41
assign out = enable ? in : {n{1’bz}};

## Slide 42: How a tri-state driver is usually used
At most one of the tri-state drivers turns on at a time
If we want A to drive the output, turn on driveA, etc.
You might think of this as a “distributed multiplexer”

## Slide 43: Details…
A built-in resolution function determines what happens when multiple values assigned.
The resolution function takes all the values being driven on a certain wire
and calculates what the resulting value on that wire should be.
input output
1 1
0 0
0, 1 x
0, 0, 0, 0 0
0, 0, 0, 1 x
z, 0 0
z, 1, 1, 1 1
z, 0, 1 x
x,x,z x
z,z,z,z z

## Slide 44: Summary
Verilog non-blocking assignment, casex
Some state machines operate on data and it makes sense to use a symbolic state table for these.
Common datapath elements and examples
Example of how to design a generic digital system composed of both a data path and a controller. You do this in Lab 6 and 7!