## Slide 1: Slide Set 17: Hardware interfaces

## Slide 2: Learning Objectives
After finishing this set of slides you should be able to:
  Describe need for flow control when connecting hardware blocks.
  Describe how ready/valid flow control works
  Describe how to tolerate latency without losing throughput using credit-based interfaces

## Slide 3
HEX0…HEX5
LEDR
SW
we can always receive something — outputs are always valid
we can always send something — inputs are always ready
Q. when is it safe to interact?
simplest kind of module interface

## Slide 4: Hardware blocks that process data
response
request
C
+
A
B
interface timing
Q. how can we reuse this module?
tprop

## Slide 5: What about sequential modules?
C
+
A
B
timing specified in terms of clock cycle delays
1 clock cycle
request on
posedge clk
read response at
next clock edge

## Slide 6: What do hardware interfaces need to specify?
request format and semantics (like software interfaces)
but also:
when is it safe to make a request?
  like a permission to write to the module
when is it safe to read a response?
  like a permission to read from the module
(possibly) which response corresponds to which request?

## Slide 7: Interfaces with fixed delays
C
+
A
B
timing specified in terms of clock cycle delays
2-clock-cycle delay

## Slide 8: Interfaces with fixed delays: more complexity
C
ALU
A
B
op
Q. how easy is it to change the implementation?
different timing for different inputs…
Q. how easy is this to specify and verify?

## Slide 9: Interfaces with fixed delays
instr
lab 6 cpu
out
Q. when can we issue the next instruction?
Q. when can we read the output?

## Slide 10: Variable timing issues
operations may take different amounts of time
  e.g., move-immediate vs add in lab 6
  variable operation delays common in real processors
easy fixed-delay solution: wait for longest possible delay
  likely significant reduction in throughput
hard fixed-delay solution: know specific delay for every operation
  hard to program: programmer has to precisely schedule ops
  hard to verify hardware: higher risk of mistakes in design / testcases
  might be impossible (e.g., loads from a memory with caches)
we need some kind of timing abstraction

## Slide 11
load
instr
rst_n
start
waiting
results
Q. how is this problem solved in lab 6?

## Slide 12: Flow control protocols
encode permissions as actual signals (module ports)
must check some signal before making a request to a module
must check some signal before reading from a module

## Slide 13
load
instr
rst_n
start
waiting
results
this is a simple flow control interface
request to start computation
response is ready
can accept next request

## Slide 14
hardware module
with flow control
ready
enable
data
valid
data
consumed
interface rules
enable only if ready
req data with enable
read resp data only if valid
signal consumed once read
request timing
response timing
[Dally 22.1.3]
Ready-Valid Flow Control

## Slide 15: Example: FIFO
specification
two operations: enq and deq
data leaves in arrival order
data does not get lost
just two flow-controlled interfaces!
  can_enq + enq = ready / enable
  can_deq + deq = valid / consumed
can_enq
enq
data
can_deq
data
deq
flexible: interface permits different FIFO depths

## Slide 16: Connecting interfaces with flow control
can_enq
enq
data
deq
can_deq
can_enq
enq
deq
can_deq
data
data
data
interfaces with flow control are composable

## Slide 17: Tolerating latency
Q. how can we get a ready signal across?
Q. how do we know it’s safe to send?
data
+ en

## Slide 18: Tolerating latency
Q. how can we get better throughput?
Q. what is the throughput of this?
data
+ en
ready

## Slide 19: Idea: credit-based interfaces
sender keeps track of the number of credits it has
  initialize to 0
  when credits ≥ 1
    send request
    decrement # credits
consumer hands out credits
  initially
    send as many credit grants to sender as we have buffer space
  when a request is processed
    send credit grant to sender

## Slide 20: Tolerating latency
data
+ en
grant
credit-based interfaces tolerate arbitrary latency

## Slide 21: Summary
fixed-latency interfaces
flow-control interfaces
composability
tolerating latency